# Introduction
This Specification contains normative information about the OpenLCB Message Network. Corresponding discussion and background can be found in the corresponding “OpenLCB Message Network Technical Note”.
The protocol is described via three components: the state machine within the node(s); the messages; and the basic interactions in which the nodes take part. These are separately described below in terms of the general format as well as specific message definitions.
Messages are transported across a specific data-link level implementation, for example using CAN frames or TCP/IP sockets. The messages are described first in general terms, then mapped to specific implementations (see Sections 8 and beyond). The states and interactions are the same across all data-link implementations.
# Intended Use
The messages and interactions described here are used by all OpenLCB nodes to connect to the OpenLCB network. They are mandatory.
## References and Context
For background information on format and presentation, see:
OpenLCB Common Information Technical Note
This specification is in the context of the following OpenLCB Specifications:
The OpenLCB Unique Identifier Specification, which specifies Unique Identifiers and how they are defined.
This specification is in the context of the following OpenLCB-CAN Specifications:
The OpenLCB-CAN Frame Transfer Specification, which specifies transfer of OpenLCB messages over CAN segments. “CAN” refers to the electrical and protocol specifications as defined in ISO 11898-1:2003 and ISO 11898-2:2003 and their successors.
This specification is in the context of the following OpenLCB-TCP/IP Specifications:
The OpenLCB-TCP/IP Segment Transfer Specification, which specifies transfer of OpenLCB messages over TCP/IP links.
Conformance with a later version of a referenced standard shall be accepted as conformance with the referenced versions.
# Messages
## Message Format
OpenLCB messages are sent using the transfer mechanism and format described in the specification for a specific wire protocol.
All messages shall contain a source Node ID and a Message Type Indicator (MTI). The MTI defines both the general format of the message and its specific type. All messages with the same MTI are of the same type.
### Message Type Indicators
The general Message Type Indicator (MTI) is a 16-bit quantity. The MTI values are remapped for specific wire protocols, see the appropriate sections of this document for adaptation to CAN and TCP/IP.
The current allocations are documented in a separate spreadsheet[1]. We keep them in just that one place to avoid conflicting updates. Those allocations are normative.
[1] See Appendix 1, and the associated TN, it provides concrete examples that may help you understand the material in this document.

MTI – Message Type Indicator
Bit(s)	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
Field	Reserved		Special	Stream or datagram	Priority		Type within Priority					Simple / Protocol	Address Present	Event Present	Modifier

MTI Bit-field Descriptions
Field Name	Bit Position	Size / bits	Mask / hex	Description
Reserved	14 - 15	2	0xC000	Reserved for future use, send and check as zero.
Special	13	1	0x2000	Operationally special, 1= forward through Gateways
Stream or Datagram	12	1	0x1000	0=Regular message, 1=Stream or Datagram message
Priority	10 - 11	2	0x0C00	Gross priority of message, 0 is highest priority
Type within Priority	5 - 9	5	0x03E0	Minor priority determination
Simple Protocol	4	1	0x0010	1=This message should be handled by simple nodes
Address Present	3	1	0x0008	1=This message has a destination address-field
Event Present	2	1	0x0004	1=This message has an event-field
Modifier	0 - 1	2	0x0003	Message-specific extra information

Note that these fields inform the intent of the message, but also the overall format of the rest of the message.

### Message Content
The message content consists of:
- The MTI
- The source Node ID
- If the MTI flags it as being present, the destination Node ID
- If the MTI flags it as being present, an Event ID
- Any other content as defined for the specific message type to a maximum of 72 bytes.
The exact format and order are defined by the specific wire protocols, but in all cases the message shall be fully decodable based on the flag-bit information in the MTI.
## States
The message network layer in an OpenLCB node has two states:
- Uninitialized
- Initialized
Nodes shall start in the Uninitialized state.
A node in the Uninitialized state may transmit an Initialization Complete message, but shall not transmit any other message type.
A node in the Initialized state may transmit any message type.

## Definition of Specific Messages
This section defines the format of common core messages. Although there is a short description of the purpose of the message, and related interactions, this is just for identification and explanatory purposes. The meaning of the messages is defined by the interactions in which they take part. These are described in later sections.
When a NodeID is present in the data content of the message, the full 48-bit identifier shall be sent for all wire protocols, specifically including CAN, even if an alias or alternate form is available elsewhere in the message.
### Initialization Complete
Indicates that the sending-node initialization is complete and, once the message is delivered, it is reachable on the network.
Name	Simple Protocol	Dest ID	Event ID	Description	MTI	Data Content
Initialization Complete	N	N	N	Full Protocol Required	0x0100	Source Node ID
	N	N	N	Simple Subset Sufficient	0x0101

This message has two MTIs, distinguished by the modifier field, to indicate whether the node requires delivery of all the messages in the full protocol, or whether delivery of the Simple Protocol subset is sufficient.
### Verify Node ID
Issued to determine which node(s) are present and can be reached.
Name	Simple Protocol	Dest ID	Event ID	Description	MTI	Data Content
Verify Node ID	-[2]	Y	N	Addressed	0x0498	Optional Full Node ID
	Y	N	N	Global	0x0490
[2] By definition, all addressed messages are received by the addressee, so the simple bit is ignored. See TN.

### Verified Node ID
Reply to the Verify Node ID message.
Name	Simple / Protocol	Dest ID	Event ID	Description	MTI	Data Content
Verified Node ID Number	Y	N	N	Full Protocol Required	0x0170	Source Node ID
	Y	N	N	Simple Subset Sufficient	0x0171

This message has two MTIs, distinguished by the modifier field, to indicate whether the node requires delivery of all the messages in the full protocol, or whether delivery of the Simple Protocol subset is sufficient.
### Optional Interaction Rejected (OIR)
This is a reply indicating failure.
Name	Simple Protocol	Dest ID	Event ID	MTI	Data Content
Optional Interaction Rejected	N	Y	N	0x0068	Error codes, MTI, optional info

The data contents are, in order:
- Two bytes of error code.
- Two bytes of MTI. If the frame transport only delivered part of the MTI[3], that content is returned with the rest of the MTI bits set to zero.
  [3] For example, in this case, CAN delivers 12+1 bits of the MTI via each frame (the special bit is known to be zero).
- Any extra bytes that the node wishes to include. There can be zero or more of these. These shall be described in the node documentation.
Nodes shall process this message even if not all of the contents are provided.
For Error Codes see section #3.5.6 Error Codes, and section #3.5 Error Handling.
### Terminate Due to Error
This is a reply indicating failure.
Name	Simple Protocol	Dest ID	Event ID	MTI	Data Content
Terminate Due to Error	N	Y	N	0x00A8	Error code, MTI, optional info

The contents are, in order:
- Two bytes of error code.
- Two bytes of MTI. If the frame transport only delivered part of the MTI[4], that content is returned with the rest of the MTI bits set to zero.
  [4] For example, in this case, CAN delivers 12+2 bits of the MTI via each frame (the special bit is known to be zero and the stream/datagram bit can be inferred).
- Any extra bytes that the node wishes to include. There can be zero or more of these. These shall be described in the node documentation.
Nodes shall process this message even if not all of the contents are provided.
For error codes see section #Error Codes and section #3.4.3.Error Handling.
### Protocol Support Inquiry
Requests that the addressed node reply with an indication of which protocols it supports.
Name	Simple Protocol	Dest ID	Event ID	MTI	Data Content
Protocol Support Inquiry	-	Y	N	0x0828	(none)

### Protocol Support Reply
Replying indicating the protocols that the node supports.
Name	Simple Protocol	Dest ID	Event ID	MTI	Data Content
Protocol Support Reply	N	Y	N	0x0668	One or more bytes identifying the supported protocols; see Table immediately below for coding.

A 1 in a bit position of the data indicates that the corresponding protocol is supported by the transmitting node. A 0 in the bit position indicates that the corresponding protocol is not supported by the transmitting node.
If a node transmits less than the full length of the currently-defined reply data, any missing bits shall be interpreted as zero.
Protocol	Protocol Flags
Simple Protocol subset	0x80 00 00
Datagram Protocol	0x40 00 00
Stream Protocol	0x20 00 00
Memory Configuration Protocol	0x10 00 00
Reservation Protocol	0x08 00 00
Event Exchange (Producer/Consumer) Protocol	0x04 00 00
Identification Protocol	0x02 00 00
Teaching/Learning Configuration Protocol	0x01 00 00
Remote Button Protocol	0x00 80 00
Abbreviated Default CDI Protocol	0x00 40 00
Display Protocol	0x00 20 00
Simple Node Information Protocol	0x00 10 00
Configuration Description Information (CDI)	0x00 08 00
Traction Control Protocol (Train Protocol)	0x00 04 00
Function Description Information (FDI)	0x00 02 00
DCC Command Station Protocol	0x00 01 00
Simple Train Node Information Protocol	0x00 00 80
Reserved for future protocol bits. Shall be sent as 0 and ignored upon receipt. / Trailing 0-bytes do not need to be sent.	All others

## Interactions
All nodes shall be able to take part in all standard interactions, as defined below.
### Node Initialization
Newly functional nodes, once their start-up is complete and they are fully operational, shall send an Initialization Complete message and enter the Initialized state. Nodes shall not emit any other OpenLCB message before the “Initialization Complete” message.
### Node ID Detection
Upon receipt of an directed (addressed) Verify Node ID message addressed to it, a node shall reply with an unaddressed Verified Node ID message.
Upon receipt of a global (unaddressed) Verify Node ID message that does not contain an (optional) NodeID, a node shall reply with an unaddressed Verified Node ID message.
Upon receipt of a global (unaddressed) Verify Node ID message that contains an (optional) NodeID, a node will reply with an unaddressed Verified Node ID message, if and only if the receiving node's NodeID matches the one received.
If a node receives multiple Verify Node ID messages before it replies to one or more, it may, but is not required to, combine multiple responses into one.
### Protocol Support Inquiry and Response
On receipt of a Protocol Support Inquiry message, a node will reply with a Protocol Support Response with bit values corresponding to the protocols that the node implements.

## Error Handling
There are multiple error-handling scenarios defined.
### Reject Addressed Optional Interaction
If a Node receives an addressed message with an MTI that is not part of the mandatory set, and it does not want to take part in that interaction, it shall send an Optional-Interaction Rejected (OIR) message addressed to the originating node, with the original MTI in the message content to indicate that the MTI is not recognized or not implemented by this node. The OIR message content may also contain a reason code and a data value, as defined by the protocol, as listed below in section 3.5.6.
### Reject Unaddressed Optional-Interaction
If a Node receives an unaddressed message with an MTI that indicates the start of an non-mandatory / optional interaction, and the Node does not want to take part in that optional interaction, it silently drops the message without reply.
### Reject Addressed Standard Interaction Due to Error
If a Node is taking part in an addressed interaction with another node, where either node may be able to send the next message, and some error condition prevents this Node from continuing the interaction, to terminate the interaction, this Node sends a Terminate Due to Error message to the other Node. It then resets its state so as to no longer be taking part in the addressed interaction. The message content contains the most recent MTI received in this interaction, a mandatory reason code and an optional data value. Although the use of these fields is to be defined, space must reserved for messages, so we specified the number of bytes.
In addition, upon receipt of the Terminate Due to Error message, the other Node also resets its state so as to no longer be taking part in the addressed interaction.
### Duplicate Node ID Discovery
OpenLCB nodes shall indicate an error when they detect an incoming message with a Source Node ID equal to their own using whatever indication technology is available. See the General Event documentation for one method of indication that uses a well-known Global-Event.

### Error codes
Numerous messages are defined to carry status information and error codes. An OpenLCB Error code is a 2-byte value of the following format:
Error Codes
Bits	Value	Description
Error Type. Exactly zero or one of the following bits shall be set:
12-15	0x8000	Accept, no error. This value shall not be used in Reject messages.
	0x4000	Reserved. Send as 0, treat it as unspecified Permanent error when received.
	0x2000	Temporary error (resend OK). Re-trying the same interaction later is likely to succeed.
	0x1000	Permanent error. Re-trying the same interaction will result in the same error.
Specific Error Enumeration:
8-11	Reserved for future use.
General Error Flags:
4-7	For Permanent error, the following flags are defined, and may be used:
	0x1080	Invalid arguments. Some of the values sent in the message fall outside of the expected range, or do not match the expectations of the receiving node.
	0x1040	Unimplemented. The functionality that the message tried to invoke is not implemented in the destination node. Also, while the transport protocol is supported, the specific data content is not recognized or not supported.
	0x1020	Source not permitted.
	0x1010	Unimplemented. The functionality that the message tried to invoke is not implemented in the destination node.
	For Temporary error (resend OK), the following flags are defined, and may be used:
	0x2080	Transfer error. The message or received message was ill-formed, failed checksum, or is otherwise uninterpretable. On CAN, this is handled by the hardware.
	0x2040	Unexpected, Out of order. An inconsistency was found in the message or frame sequence received, the arrived message is unexpected or does not match the state of the receiving node.
	0x2020	Buffer unavailable or destination node busy.
Additional flags:
0-3	Reserved for use of specific protocols for error reporting. Interpretation of these bits will be defined in the specific protocol documentation. A value of zero in this field means no further information is available.

NB: Nodes may return 0x0000 as an error-code.
## Routing
All messages may be, but don't have to be, presented to every node for processing.
Addressed messages shall to be routed to the addressed node. The node transmitting an addressed message addressed to itself shall take part in any interactions required by the message.
Unless otherwise specified in a protocol document, global messages shall be forwarded to all nodes. The node transmitting a global message shall take part in any interactions required by the message.
## Delays and Timeouts
Nodes shall send messages required by OpenLCB protocols within 750 milliseconds, unless otherwise indicated in the documentation for the specific protocol interaction.
Nodes may, but are not required to, use a timeout mechanism to protect against messages lost due to malfunctions. Such a timeout shall not be shorter than 3 seconds.
# Simple Node Protocol Subset
OpenLCB uses the “Simple Node Protocol” concept to distinguish a subset of global message types that are never needed by certain “simple” nodes. They can then be rapidly ignored by those nodes, and gateways can filter them from segments that contain only simple nodes, etc. It is not normative.
## Protocol Description
Operationally, the simple node protocol is defined by the MTIs that carry a set Simple Node bit, plus all addressed messages. This section summarize received transmitted messages, and describes the reasoning behind those choices in the current MTI definitions.
### Messages Transmitted
Simple nodes may transmit any message, which shall be propagate normally.
### Messages Received
Simple nodes shall receive any message specifically addressed to them, plus the following unaddressed global messages:
- Verify Node ID ;
- Verified Node ID;
- Protocol Support Inquiry;
- Identify Consumers;
- Identify Producers;
- Identify Events;
- Learn Event;
- P/C Event Report;
In the future, additional MTIs will be defined. If simple nodes need to received them, the MTI will indicate that via the Simple bit – see previous section.
### Messages Not Received
Messages not listed in the section above do not need to be received by simple nodes.
# Gateway Processing
No Standard content, see TN for discussion.
# Expansion
No Standard content, see TN for discussion.
# CAN Adaptations
## Introduction
This section specifies how the Common Protocols are mapped to the CAN. While CAN is relatively inexpensive and robust, it is limited by its bandwidth and its total frame size, which is about 12-bytes, and by its speed (125 kbps). Each CAN frame includes a header (29-bits) and a data-part (8-bytes). In addition, the CAN-header has special properties which both enhance and limit its use. The Common Messages are adapted to CAN by:
- The Common-MTI is shortened to 12 bits, and carried in the header.
- Node IDs are shortened to 12 bit CAN-Aliases.
- Longer messages are fragmented into one or more CAN-frames. Special frames formats are used to implement Datagrams and Streams.
These mappings result in a set of modified formats as documented in this section. This section's numbering parallels that of the Common sections.

Common Message	CAN Mapping	Comment
Most messages	Usually single frame	Multiple frames are used for longer messages.
Datagram	First-, Middle-,…, Last- frames	Small Datagrams may be carried by a single Only-frames.
Stream	Stream-Data-frames	A common Stream-message will be mapped to one or more Stream-Data-frames.

## Intended Use
CAN is intended a local transport for smaller layouts, or for local segments for larger layouts. Accommodation and specialization is necessary to implement the protocols onto CAN because CAN frames are limited to about 12 bytes of information. The main mappings include a shortened CAN-MTI (12-bits) and the use of 12 bit aliases for Node Ids. These have implications for Gateways which are specified below.
### References and Context
This specification is in the context of the following OpenLCB-CAN Specifications:
The OpenLCB-CAN Frame Transfer Specification, which specifies transfer of OpenLCB messages over CAN segments. “CAN” refers to the electrical and protocol specifications as defined in ISO 11898-1:2003 and ISO 11898-2:2003 and their successors.
## Messages
### Message Format
The CAN mapping uses several formats. The general form of the CAN header is:
29-bit CAN Header
Field		CAN prefix		Frame Type		Variable Field					Source ID
Size & location		2 bits / 0x1800,0000		3 bits / 0x0700,0000		12 bits / 0x00FF,F000					12 bits / 0x0000,0FFF
Value(s)		3		1,2,3,4,5,or 7		CAN-MTI or Destination Node Alias					Source Node Alias
Up to 8 Byte Data-Part
Byte#	0		1		2		3	4	5	6		7
Values	variable		variable		(Data)		(Data)	(Data)	(Data)	(Data)		(Data)

Table 1: CAN Frame Format
CAN frames also contain other bit fields not detailed here, including a DLC or length field.
#### CAN Prefix Field
The CAN Prefix Field contains control bits specific to CAN.
#### CAN MTI Mapping
The Common MTI is mapped to one of eight frame types:
Frame Type	Meaning
0	(Reserved)
1	Global & Addressed MTI
2	Datagram complete in frame
3	Datagram first frame
4	Datagram middle frame
5	Datagram final frame
6	(Reserved)
7	Stream Data

Table 2: CAN Frame Type Values
#### Global and Addressed Messages, CAN Frame Type 1
Global and Addressed messages are those Common MTIs with the “stream and datagram” bits unset, and are mapped to and from CAN MTI type 1.
The CAN MTI is carried in the CAN header. It consists of the lowest-order 12 bits of the Common MTI, and, by implication has the “stream or datagram” and “special” bits as zeros.

29-bit CAN Header
Field		CAN prefix	Frame Type	Static Priority	Type within Priority		Simple Node flag		Address Present		Event ID present		Modifier Bits		Source ID
Size & location		2 bits / 0x1800, / 0000	3 bits / 0x0700, / 0000	2 bits / 0x00C0, / 0000	5 bits / 0x003E, 0000		1 bit / 0x0001,0000		1 bit / 0x0000, / 8000		1 bit / 0x0000,4000		2 bits / 0x0000, / 3000		12 bits / 0x0000,0FFF
Value(s)		3	1	CAN-MTI					Source Node Alias
Up to 8-Byte Data-Part
Byte#	0			1		2		3		4		5		6		7
Value	Optional Flags/Destn Alias or (Data)					(Data)		(Data)		(Data)		(Data)		(Data)		(Data)

Table 3: CAN Frame Type 1 Format
If the “addressed” bit is set to 1, then the destination address is placed in the 1st two bytes of the data part of the CAN frame: the top nibble of the 1st byte contains flags (see below); the lower nibble of the 1st byte and the entire 2nd byte contain the 12-bit destination alias.
The format of this in binary is: 0brrff dddd, dddd dddd (or in hex: 0xfddd)
where:
- The two rr bits are reserved, and read and send as zeros.
- The two ff bits can be used for packing and unpacking large messages to a sequence of CAN frames, see below. The coding is:
- 00 Only frame
- 01 First frame of more than one
- 10 Last frame of more than one
- 11 Middle frame of more than 2.
- You can think of these as active-zero start and end bits, respectively.
- Messages are limited to 72 bytes of data.
CAN frames marked as First or Middle frame shall carry eight total data bytes. CAN frames marked as Last or Only frame shall have from two through eight total data bytes.
#### Datagram and Stream Messages, CAN Frame Types 2-5 and 7
Frame Types 2-5 and 7 are used specifically for Datagram and Stream messages.

### States
No special provisions for CAN transport layer.
### Definition of Specific Messages
CAN messages definitions parallel the common messages in section #3.3.Definition of Specific Messages.
#### Initialization Complete
Name	Description	CAN-MTI	CAN Header	Data Content
Initialization Complete	Full protocol	0x100	[0x19100sss]	Full Source Node ID
	Simple-set sufficient	0x101	[0x19101sss]

#### Verify Node ID
Name	Description	CAN-MTI	CAN Header	Data Content
Verify Node ID	Addressed	0x498	[0x19498sss]	fddd[5], Optional Full Node ID
	Global	0x490	[0x19490sss]	Optional Full Node ID
[5] “fddd” refers to a flag-nibble “f”, containing multipart flags, and the 12-bit Destination Node Alias “ddd”. See TN.

#### Verified Node ID.
Name	Description	CAN-MTI	CAN Header	Data Content
Verified Node ID	Full protocol	0x170	[0x19170sss]	Full Source Node ID
	Simple-set sufficient	0x171	[0x19171sss]

#### Optional Interaction Rejected
Name	CAN-MTI	CAN Header	Data Content
Optional Interaction Rejected	0x068	[0x19068sss]	fddd, error, optional info

#### Terminate Due to Error
Name	CAN-MTI	CAN Header	Data Content
Terminate Due to Error	0x0A8	[0x190A8sss]	fddd, error, optional info

#### Protocol Support Inquiry
Name	CAN-MTI	CAN Header	Data Content
Protocol Support Inquiry	0x828	[0x19828sss]	fddd

#### Protocol Support Reply
Name	CAN-MTI	CAN Header	Data Content
Protocol Support Reply	0x668	[0x19668sss]	fddd, Protocol flags

This shall be a multi-part message when there are more than 48 protocol-bits.
### Extensibility
Since the earlier nodes may reply as soon as they have processed only the data of which they are aware, their replies may be earlier than the last message fragment is received. Sending-nodes shall be able to receive and process these replies as they are received.
### Interactions
No special provisions for CAN transport layer.
### Error Handling
No special provisions for CAN transport layer.
### Routing
CAN implementations shall send the frames of a message together to reduce buffering. Higher-priority messages may be sent in the middle of a lower-priority message.