# Introduction
This Technical Note contains informative discussion and background for the corresponding “OpenLCB Unique Identifiers Standard”. This explanation is not normative in any way.
# Annotations to the Standard
This section provides background information on corresponding sections of the Standard document. It's expected that two documents will be read together.
## Introduction
Originally, OpenLCB was defined in terms of 48-bit unique “Node IDs”. Other uses were found for these IDs that didn't associate them with a specific node, which demonstrated the need for Unique Identifiers beyond just Node IDs. Therefore, the Standard and this Technical Note are generally written in terms of Unique Identifiers, which includes Node IDs usage.
## Intended Use
The "globally unique" requirement only refers to the universe of connected nodes; nodes that never need to communicate with each other need not have separate Node IDs. In general, however, nodes can move: they can be sold or loaned for use on another layout, nodes on modular layouts can be connected to other arbitrary modules, and few assumptions can be made. It is best if nodes are given a completely unique identifier when manufactured, so there's no need to ever detect and resolve a conflict. If a Node ID conflict should occur on an OpenLCB network, there is no specified way in which the conflict shall be dealt with. The conflict may (or may not) be reported, and there may (or may not) be an automatic recover mechanism in place. OpenLCB standards place the effort and burden on preventing a conflict from occurring rather than resolving a conflict if it does occur.
## References and Context
This technical note is in the context of the following OpenLCB Standards:
- The Message Network Standard, which defines the basic messages and how they interact. Higher-level protocols are based on this message network, but are defined elsewhere.
- The Event Identification Standard, which defines the well-known Events Identifiers.
## Content and Format
The Standards don't require any particular human-readable format for input and output, but hex-pairs with separators (example: 01.AB.34.01.CD.E3) are recommended by the Common Information TN. If any other format is used, including decimal pairs, it's very important to make it clear how to interpret it.
There are many methods to store a Unique Identifier, and that's not constrained by this Standard. It could be stored in a non-volatile memory, as jumpers on a board, etc.
## Allocation
Unique Identifiers are assigned via a delegation process. At the highest level, ranges are assigned to people and organizations, within which they are responsible for assigning unique identifiers to separate devices. These ranges can be subdivided and delegated further, as needed. Additional ranges can then be requested, which will eventually be recorded in the Unique Identifier Standard. The OpenLCB organization reserves the right to allocate Unique Identifiers within a separate database in real-time and periodically update the Unique Identifier Standard document from this database. In the unlikely event that a conflict shall arise between OpenLCB managed real-time database and the Unique Identifiers Standard, the Unique Identifiers Standard, the Unique Identifiers Standard document represents the true allocation.
One of the reasons for having a long, 48-bit Unique Identifier space is to make it easier to use a delegation system like this. Because there are a lot of possible Unique Identifiers, large ranges can be delegated to groups without having to ensure that the range be efficiently used. For example, most NMRA members will not design their own OpenLCB nodes and need to assign node IDs, but assigning a range to every member makes it easy for those who want to, at a total cost of only 0.0016% of the available Unique Identifier space.
In the delegated assignments, the lower order byte(s) are self-assigned. The value of zero should be reserved, indicating that a number within the range hasn't been assigned.
The high byte of each range is different for each type of assignment, making it easy to determine the allocation pattern in use for a particular Unique Identifier.
Allocations are meant to be unique forever, so the specification requires that new allocation ranges not overlap existing ones, and allocation regions not be reused later.
### Globally defined Unique Identifiers
In addition to use as node identifiers (node IDs), OpenLCB unique identifiers are used to ensure uniqueness of specific global event identifiers and for other purposes. These numbers must be allocated so that they are kept unique. The identifiers specified in this section are of that type.
Note that the detailed use of these identifiers is specified elsewhere. In some cases, the protocols are still being developed, and the entry here is just reserving a range for a specific future use.Manufacturer Specific
faults” doesn't lose the self-assigned part of the Node ID (example: the serial number).
### Well-Known Global Identifiers
In addition to use as node identifiers (node IDs), OpenLCB unique identifiers are used to ensure uniqueness of specific global event identifiers and for other purposes. These numbers must be allocated so that they are kept unique. The identifiers specified in this section are of that type.
Note that the detailed use of these identifiers is specified elsewhere. In some cases, the protocols are still being developed, and the entry here is just reserving a range for a specific future use.
### Self-Assigning Groups
MERG kit builders and others would like to assign their own identifiers without going through a complicated process. To make this possible without any interaction with anybody, these groups are assigned identifier ranges that involve their member number in the organization. A member may assign any identifier from this range to the node(s) they produce, provided that each identifier is assigned to at most one node. A range of 255 identifiers per member is typically sufficient for hobby usage. Should a hobbyist exhaust their assigned range, the hobbyist can get another, larger assignment. It's also convenient to give hobbyists a byte as their range.
Each organization is assigned a unique high-order two bytes. The organization member number is given 24 bits. Byte 2 of the Unique Identifier advances by 4 between groups (NMRA is 0x00, MERG is 0x04, etc) to allow a little more headroom on group membership numbers; this space can be reclaimed later if needed.
Other groups have defined mechanisms to ensure that their node numbers or equivalent constructs are uniquely assigned. They may have non-technical reasons for wishing to use those same mechanisms to assign OpenLCB unique identifiers. Ranges of OpenLCB Unique Identifier ranges can be assigned to these groups, so that when people then use the group's mechanism to select a value within that range, the result will be a properly unique OpenLCB Unique Identifier.
The first example of this is MERG CBUS developers. MERG CBUS has defined a “no cost” way of identifying unique 16-bit Node Number (NN) for CBUS use, perhaps with an optional 16-bit Layout Number (LN). People who wish to use this mechanism to allocate unique OpenLCB Node ID identifiers can, without having to consult anybody, generate an OpenLCB Node ID from the unique CBUS number(s) as described in the Standard.
If the user is involved in determining the Unique Identifier for a node (the Node ID) by setting switches, the possibility of duplicated Node IDs must be considered. Users make mistakes. To reduce user frustration, the node should provide a user-visible way to indicating a duplicate has been seen, and should fully implement the relevant wire-protocol-specific methods for detecting duplicate Node IDs.
### Assigned by Software at Runtime
Programs that act as one or more OpenLCB nodes need to associate unique identifiers with them. For licensed software, where a unique key can be associated with each instance of the program, this is easy: Use the manufacturer space defined above, and generate the lower bits of a specific ID from the license key.
Free, open and unlicensed software can't use a license-key-based method. Unfortunately, the 48-bit address space is too small to use the IP-address-plus-signature GIDs that would otherwise make this a simple problem, or the even larger MAC-address-plus-signature GIDs.
Initial experiments were done using 32-bit IPv4 addresses as components of Unique Identifiers, but this is no longer recommended for several reasons:
- Not all IPv4 addresses are globally unique. Some IP addresses correspond to “private networks”, which are only locally unique. See RFC 1918 and RFC 3330 for more information. In addition, Microsoft defined an non-IETF “Automatic Private IP Addressing” mechanism for providing non-global IP addresses.
- A single computer may run several programs, so there still needs to be separate mechanism to provide a unique value for the lowest bytes of the ID. That involves a level of coordination across multiple software vendors that's hard to imagine.
- IPv6 is coming. It provides addresses that are too large to use directly. Even before that happens, the various issues of IPv4 to IPv6 mapping raise all sorts of questions about uniqueness of IPv4 addresses.
- Even globally routable IPv4 addresses may not be unique over time. For example, DCHP may assign the same address to multiple computers sequentially. This is particularly an issue with wireless access at e.g. clubs and shows.
Computers that have global Internet access, even if they don't have a permanent and unique IP address, can still get a Unique Identifier from an openlcb.org-provided service. These Unique Identifierss are provided from a specified range to ensure that they are unique when created. Each identifier is only provided once to ensure that it remains unique. Programs using this facility should permanently remember Unique Identifiers obtained this way, because they won't get the same one on a later request.
Other organizations can also distribute Unique Identifiers from within their allocated blocks. For example, a Unique Identifier could be provided when a free-software program is downloaded, perhaps as part of the download package or even as part of its filename.
Programs without access to an ID-providing service must use some other mechanism, which may result in prompting the user for a Unique Identifier assigned by one of the other mechanisms.
### Specifically Assigned by Request
Users can request blocks of Unique Identifiers of various sizes. The small (256) and medium (65536) blocks are not scarce resources. Requests for these blocks should be routinely granted once the requester has been identified. The 24-bit blocks are slightly scarcer, but there are still almost 216 of them available by using additional values for byte 2.
An initial automated system for requesting and obtaining unique ID ranges is available at http://openlcb.org/trunk/web/requestuidrange.php and subsequent pages.
### Locomotive Control Systems
Locomotive control was initially beyond the scope of OpenLCB development, but later work started to define OpenLCB methods for working with existing locomotive control systems. This section specifies ranges of Unique Identifiers that are reserved for the purpose of interfacing with locomotive control. The details of how there are to be used are specified elsewhere, but sufficient range has been reserved to allow providing decoders with OpenLCB unique identifiers, etc. It is important to note that at the time of this document's publication, locomotive control does not require any of these Unique Identifiers. For this reason, this Unique Identifier range is considered deprecated. Do not use these Unique Identifiers for any reason, they are no longer valid.
### RFID and NFC
The RFID and NFC Unique Identifiers space is reserved to be used in future standards to be defined elsewhere.
### Reserved Unique Identifiers
For error detection, we permanently reserve all identifiers that start with either a 0x00 or 0xFF value. OpenLCB implementations should, but are not required to, treat it as an error when any of those are encountered.
### Temporary Assigned by Software at Runtime
As described in the section 2.5.4 Assigned by Software at Runtime above, there are many reasons for which a node may want to be assigned a Unique Identifier at runtime. This Unique Identifier space is specifically designated for temporary (leased) assignment of these Unique Identifiers. There is a contract implied with the assignment between the server and client that is valid for a time period defined by the server. Once the prescribed time period expires, the client node must cease usage of the previously assigned Unique Identifier.
The implementation of the client server protocol is not explicitly defined, and may use non-OpenLCB mechanisms, such as a TCP connection over the Internet. The following list suggests implementation details that are not required, but might be considered when designing such a client server pair:
- Lease time can be extended through a renewal process.
- The server does not reassign a previously assigned Unique Identifier until it has run through the entire pool allocated to it.
- The server allows the client to suggest a Unique Identifier that it would like form the server's pool.
- The client remembers its last Unique Identifier assignment and suggests to the server to be re-assigned this Unique Identifier upon reset, power failure, or disconnection from the server.
# Implementation Information
Specific Unique Identifier assignments are stored in a MySQL database on the http://openlcb.org website. The full list of assignments, include overall ranges from the specification and ranges assigned for specific purposes and users, can be found on the http://www.openlcb.org/trunk/web/viewuid.php dynamic page.
Automated allocation systems can be abused, and we don't want to give away large chunks of address space to automated requesters. All available information about requests is logged. Users are asked for their name and contact information at the time of the request, which is also logged. Depending on our experience with requests, we may have to add an email challenge-response or other mechanism to ensure only valid requests get allocations.