# Introduction
This explanatory note contains informative discussion and background for the corresponding “OpenLCB CAN Message Network Specification”. This explanation is not normative in any way.
# Annotations to the Specification
This section provides background information on corresponding sections of the Specification document. It's expected that two documents will be read together.
## Introduction
## Intended Use
## References and Context
## Message Format
## Messages
## Interactions
# Message Type Indicator Definition

The MTI is a 16 bit quantity, but it can be shoe-horned into small spaces as needed for CAN efficiency. (Need a section on mapping?)
MTIs are 15 bits max in a CAN header, due to the size of the variable field, or 16 bits if carried in the data.

Below this is just a collection of pieces from other docs right now.
The priority bit in the CAN frame is separate from the static priority field in the MTI format specification.

The specific MTI values are being allocated in each protocol definition, and also here for consistency checks.
In general, the MTI selection is done on the top 8 bits of the variable field. This is mapped to the low MTI byte in a standard format message.

Some MTIs have additional status bits defined as part of the 2nd field. For example, there are two status bits associated with “Consumer Identified” which must be kept in the header since there is no room in the CAN data field. To simplify translation between formats, these are the low bits of the first byte after the MTI in a standard-form message.
Designers may wish to use CAN hardware filtering, but it can't be assumed to be present. We assign a single bit to indicate “simple node protocol” messages to make simple filtering possible.

Design decisions:
A specific mapping from the common 16-bit MTI format to a shorter CAN format is documented in a separate worksheet (PDF version). The common form is 16 bits to have lots of space to grow at the high end, but it can be mapped into a 8 bit field for efficient CAN transfer.

## OpenLCB Common Message Format
A common message consists of several parts:
- Node ID Number of the Source node (SID)
- Message Type Indicator (MTI)
- In some cases, the Destination Node ID (DID)
- In some cases, a P/C Event ID (EID)
- Message content, as defined by the particular message type
Each OpenLCB wire protocol may define local representations for each of these components at the transport level and below. This may involve replacement (e.g. using a shorter "Alias" token for the node ID number), reordering, and/or specific representations that differ from the common ones, but in all cases it must be possible to translate from the wire protocol message to a complete common message using only locally available information.
By convention, multi-byte quantities in OpenLCB are represented in big-endian order. The most significant byte is sent first, and stored at the lowest address. This is the same as Ethernet and the common internet protocols, but not the same as the Intel x86 architecture.
Reserved quantities must be created with a zero value unless otherwise specified. When processing a message, any reserved quantities must be ignored unless otherwise specified. When transporting a message, reserved quantities must be transported unchanged. The zero value sometimes indicates a non-initialized value.

Message Type Indicator (MTI)
The common Message Type Indicator (MTI) is a 16 bit quantity.
Each specific MTI has a specific defined content documented elsewhere, but there are a few general points.
- Messages are variable length. The specific wire protocol is responsible for carrying length information as needed.
- If the message carries a destination address, that destination node ID (destination address) is the first part of the message content. The form of a Destination Node ID is defined by the particular wire protocol, but must be mappable to the full Node ID of the intended destination.

The common Message Type Indicator (MTI) is a 16 bit quantity. Note that specific wire protocols may remap this.
- The most-significant 5 bits are reserved as 00110; nodes must send and check that value.
- The next 7 bits are used to indicate the message type.
- The top two of these are used to form static priority groups. A 0 bit is considered to have more priority (can be processed first), a 1 bit less priority (can be processed later). The MSB makes a larger statement about priority than the LSB of these two. Priority processing is permitted but not required. The priority group bits are part of the overall message type.
- The next bit is reserved as 0; nodes must send and check that value.
- The lower four bits indicate a specific type.
- The following bit is reserved as 0; nodes much send and check that value.
- The 2nd from-least-significant bit indicates that this message carries a destination node address (DID) when set to 1. Setting 0 means that the message is globally addressed. If a Destination Node ID (DID) is present, it is located at the start of the message content. The form of a Destination Node ID is defined by the particular wire protocol, but must be mappable to the full NID of the intended destination.
- The next-to-least-significant bit indicates this message carries a P/C Event ID field when set to 1. Setting 0 means that the message does not carry a P/C event ID. If a P/C Event ID is present, it's at the start of the message, except after the Destination Node ID, if present.
- The least-significant bit when set to 1 indicates this message carries a flag byte after the DID and/or EID determined by the above bits. The low bits of that byte can be relocated in CAN messages, see the definition of the CAN wire protocol.
We've chosen to allocate bit fields to make decoding simpler; if possible, aligned on nibble boundaries to make it easy to read as hexadecimal numbers. Note that, as a special dispensation for CAN, higher priority messages (MTIs with lower numerical values) may pass lower priority ones; this must be taken into account when designing protocols.
Specific values are allocated and documented in a separate worksheet (PDF version). We keep them in just that one place to avoid conflicting updates.

# OpenLCB message format
(rationalize with the frame doc, that describes the 1st bit)
OpenLCB common messages are carried in frames with a 1 in the Frame Type field. They contain message type information and/or address information in the 15-bit variable field, and zero to eight CAN data bytes.
For OpenLCB messages, the variable field is used in two forms:
- Unaddressed messages – messages that don't have a destination address put the low 12 bits of the MTI in the variable field
- Addressed messages – messages that have a specific destination address put it in the variable field, and carry the MTI in the payload. This allows filtering.
The variable field is allocated:

Variable Field Bits 0-2 / Header Bits 2-4 / OpenLCB Format / 0x0700,0000	Variable Field Bits 3-14 / Header Bits 5-16 / OpenLCB Variable Header Content / 0x00FF,F000
0 0 0	MTI & additional information for “simple node” unaddressed messages
0 0 1	MTI & additional information for unaddressed messages other than “simple node” forms
0 1 0	(Reserved, must not be sent or accepted)
0 1 1	(Reserved for long-form MTIs in data area, must not be sent or accepted)
1 0 0	Destination Alias for datagram message non-last fragment
1 0 1	Destination Alias for datagram message last fragment
1 1 0	Destination Alias for non-datagram addressed messages
1 1 1	Destination Alias for Stream Data Send messages

Putting the destination alias in the header allows filtering on it with common CAN hardware. Putting the Stream ID in the header also allows filtering, and preserves the full 8-byte CAN payload for stream data.
The specific MTI values are being allocated in a separate worksheet (PDF version). In general, the MTI selection is done on the top 8 bits of the variable field. This is mapped to the low MTI byte in a standard format message.
Some MTIs have additional status bits defined as part of the 2nd field. For example, there are two status bits associated with “Consumer Identified” which must be kept in the header since there is no room in the CAN data field. To simplify translation between formats, these are the low bits of the first byte after the MTI in a standard-form message.

Standard Interactions
All nodes must be able to take part in all standard interactions.
A) Node Initialization
Newly functional nodes, once their start-up is complete and they are fully operational, must send an "Initialization Complete" message.
- There is no guarantee that any other node is listening for this. No reply is possible.
- Nodes must not emit any other OpenLCB message before the “Initialization Complete” message.
Sending the IC message is required to insure that higher-level tools are notified that they may start to work with the node.

After the IC message is sent, and before any corresponding Producer/Consumer Event Report messages are sent, the node must identify all events produced or consumed on the board via zero or more Identify Consumers, Identify Consumed Range, Identify Producers and Identify Consumed Range messages. These are not required to be in any particular order.
B) Duplicate Node ID Detection
OpenLCB nodes must have unique node IDs. To detect this across the entire connected OpenLCB, all OpenLCB nodes must indicate an error if they detect an incoming message with a Source Node ID equal to their own. If possible, they should indicate it at the board itself using a light or similar. If possible, they should emit a PCER message with the “Duplicate Source ID detected” global event, which will carry the duplicate event ID in the Source Node ID field.
After sending the “Duplicate Source ID detected” global event, the node should not transmit any further messages until reset because this message will be received at the other duplicate-ID node(s), resulting in additional “Duplicate Source ID detected” global events and causing a possible message loop.
To further improve the reliability of this detection, OpenLCB nodes should, but need not, emit a Verified Node ID message every 30 to 90 seconds. As an implementation detail, it's recommended that CAN-attached nodes use their NIDa to pick that interval so that messages don't bunch up.
C) Node ID Discovery
Upon receipt of a Verify Node ID Number message addressed to it, or an unaddressed Verify Node ID Number message, a node will reply with an unaddressed Verified Node ID Number.
This can be used as check that a specific node is still reachable. When wire protocols compress the originating and/or destination NID, this can be used to obtain the full NID.

The standard Verify Node ID Number interaction can be used to get the full 48-bit NID from a node for translation. At power up each node must obtain a alias that is locally unique. Gateways will also have to obtain unique aliases for remote nodes they are proxying on to the segment.

E) Error Handling
There are multiple mandatory error-handling scenarios defined.
Reject Addressed Optional Interaction
Node A receives an addressed message from Node B that carries Node A's NID.
The MTI indicates the start of an optional interaction.
If Node A does not want to take part in the optional interaction, it may send an Optional Interaction Rejected message addressed to Node B with the original MTI in the message content. There is no requirement that OIR be sent; the node may silently ignore the incoming message.
The message content also contains an optional reason code and an optional data value. The use of these fields is to be defined.
Reject Unaddressed Optional Interaction
- Node A receives an unaddressed message from Node B.
- The MTI indicates the start of an optional interaction.
If Node A does not want to take part in the optional interaction, it silently drops the message without reply.
Reject Addressed Standard Interaction Due to Error
- Node A is taking part in an addressed interaction with Node B. Either node may be able to send the next message.
- Some error condition prevents Node A from continuing the interaction.
- To terminate the interaction, Node A sends a Terminate Due to Error message to Node B. It then resets it's state so as to no longer be taking part in the addressed interaction.
The message content contains the most recent MTI received in this interaction, a mandatory reason code and an optional data value. The use of these fields is to be defined.