# Introduction (Informative)
This specification describes the protocol for transporting OpenLCB datagrams via CAN segments.
# References and Context (Informative)
This specification is in the context of the following OpenLCB-CAN Specifications:
The OpenLCB Message Network Specification, which specifies …
The OpenLCB Node Identifier Specification, which specifies …
The OpenLCB Event Identifier Specification, which specifies ...
“CAN” refers to the electrical and protocol specifications as defined in ISO 11898-1:2003 and ISO 11898-2:2003 and their successors.
For more information on format and presentation, see:
OpenLCB Common Information Technical Note

External certification of parts shall be accepted for conformance to these standards. Conformance with a later version of a standard shall be accepted as conformance with the referenced versions.

(See TN, which contains dev note content, which needs to be move here)

## Error Codes
DATAGRAM_REJECTED 0x0000
 DATAGRAM_REJECTED_PERMANENT_ERROR 0x1000
 DATAGRAM_REJECTED_INFORMATION_LOGGED 0x1010
 DATAGRAM_REJECTED_SOURCE_NOT_PERMITTED 0x1020
 DATAGRAM_REJECTED_DATAGRAMS_NOT_ACCEPTED 0x1040
 DATAGRAM_REJECTED_BUFFER_FULL 0x2000
 DATAGRAM_REJECTED_OUT_OF_ORDER 0x6000
 DATAGRAM_REJECTED_NO_RESEND_MASK 0x1000
DATAGRAM_REJECTED_RESEND_MASK 0x2000
DATAGRAM_REJECTED_TRANSPORT_ERROR_MASK 0x4000