# Introduction
This glossary provides working definitions and commentary on definitions for OpenLCB. It is not normative in any way.
We provide a separate section of “Key Terms” for initial reading.
# Key Terms
Event
OpenLCB allows nodes to notify each other when specific "events" occur on the layout. These in turn can cause nodes to take particular actions. Events are not necessarily attached to a producer ('Button 2 pressed') or attached to a consumer ('Turn off light 4'), but rather to an overall state change ('Set for nighttime operation'). This is called a "Producer/Consumer model".
Node
A “node” is the basic unit of addressability in OpenLCB. It can be a single board, or a process in a larger computer, or any other independent actor on the OpenLCB network.
Every OpenLCB interaction originates in a node. Every board that connects to OpenLCB is at least one node. For example, a simple turnout controller board is one node, while a PC with multiple programs running may contain several nodes.
Message
The basic unit of OpenLCB communication. OpenLCB nodes exchange messages to control communications and to move information. It may take several messages to move a single datagram, or to start a stream, for example.
Protocol
An OpenLCB protocol defines how messages are exchanged to do some particular thing. There are low level protocols for things like sending datagrams, exchanging events, and doing link start-up. Higher-level protocols then define how configuration information is exchanged, or a nodes memory can be read, or a message can be put on a display.
# General Glossary

Addressed
An “addressed” message is meant for only a single node. Contrast “global”.
Alias
Short form of a Node ID (NID) number which can be mapped back and forth to the full number. Often used with a modifier, as "NID Alias", "DID Alias" or "SID Alias"", where DID and SID are specific types of Node ID (see below) and which are then written NIDa, DIDa and SIDa.
Automatically Routed Event
The Event transfer protocol defines a series of messages that determine where Event messages must be routed. Automatically Routed Events are events within a particular part of the EventID space that are routed to all nodes, without using those messages. See the Event transfer protocol documentation for more information.
Board
Not really something that occurs in OpenLCB itself, we need to talk about how the common term "board" maps onto OpenLCB. E.g. A node (board) may connect to several things (devices) on the layout.
Bridge
Connects two OpenLCB segments with minimal changes to the content of the messages. For example, a bridge between two CAN segments would allow more nodes to be attach to the combined segments as if they were one; a bridge between a CAN segment and Ethernet segment would transform message format, but transfer every message.
CDI
“Configuration Definition Information”, the information provided by a node so that other nodes can understand what the configuration information in the first node includes, and how it's organized.
Datagram
The actual data content transported by the Datagram Protocol. This can be up to 72 bytes.
Datagram Protocol
The datagram protocol is a way for a OpenLCB node to efficiently send a short, definite-length message to another specific node. In that, it lies in between the event exchange protocol, which efficiently sends very short event IDs to all interested nodes, and the streaming protocol, which sends long messages between specific nodes, at some cost in efficiency. Sending a datagram takes multiple messages.
Datagram Protocol ID (DPID or DPI)
The first byte of data transferred by a datagram is used to indicate the protocol being transported.
Device
Not really something that occurs in OpenLCB itself, we need to talk about how the common term "device" maps onto OpenLCB. E.g. A node (board) may connect to several things (devices) on the layout..
Destination Node ID (DID)
 Node ID of the node to which a specific message is addressed.
Event Exchange Protocol
Using PCER messages to propagate Event IDs from multiple source nodes to multiple destination nodes. These are typically used to announce that something of interest has happened on the layouts so that controlled devices can respond. Also includes inquiry and response messages for examining configuration and status.
Event ID (EID)
The number that identifies a specific event. OpenLCB event IDs must be globally unique.
Events are not associated with any particular node. It may be convenient to use e.g. Node ID as a way of numbering them uniquely, but Node IDs and Event IDs are not related.
Gateway
Connects two segments of the OpenLCB while translating to a different wire protocol. For example, a gateway can change NodeIDs on one side of the Router into aliases on the other side. The use of unique identifiers in OpenLCB is meant to reduce the need for gateways. They generally only appear to connect the wider network to a CAN link.
Global
A “global” message is meant for all OpenLCB nodes that are interested in it. Contrast “Addressed”.
Installation
An OpenLCB installation is the complete set of OpenLCB hardware, nodes, etc, that can be reached from any one of them.
Message Type Indicator (MTI)
Every OpenLCB message contains a Message Type Indicator field that identifies the type of that particular message. Also used to refer to a particular value for that field.
Node ID (NID)
Number identifying a specific node. OpenLCB node IDs must be globally unique, so they form a one-to-one mapping to the nodes themselves.
Producer/Consumer Model
A way of thinking about communications on a layout network. Events (unique messages on the layout network) are “produced” by some node(s), and “consumed” by other node(s). An event indicates something happened, but the corresponding message isn't necessarily a status report or a command for something to change; it's just an announcement of the event. That event can be produced by many different sources (e.g. the “use passing siding” event could be produced by a push button at either end of the siding, or on a dispatcher panel), and can be consumed by several sources (it can turn on lamps on a panel, set turnouts in multiple places, etc).
Producer-Consumer Event Report (PCER)
OpenLCB message type sent globally by producers of a particular Event to indicate that it has occurred, so that the corresponding consumers of that Event are notified.
Repeater
Connects two segments of the same type at the physical level, without transformation of message format.
Router
OpenLCB routers forward traffic from one link to another without reformatting. This can be a simple as receiving on one link and forwarding on N, or it could involve tracking e.g. event usage and only forwarding needed messages.
Source Node ID (SID)
The Node ID of the node which originated a specific message.
Segment
Subset of an overall OpenLCB installation which is reached via path or gateway. A segment typically uses a specific wire protocol.
Simple Node
A “simple node” is typically an individual board with a small processor on it which is acting a as leaf node in an OpenLCB network. A simple node doesn't initiate complex communications with other nodes, but may be the target of e.g. configuration operations.
Stream
Streams are a method of moving a large number of bytes between two nodes. The streaming protocol defines a way to do this in OpenLCB.
Streaming Protocol
Protocol that defines the messages and interactions to setup a stream transfer, move the data along with the necessary buffer management, and then take down the transfer at the end. Streams are efficient ways to move large amounts of data when the setup and take-down process can be considered a negligible part of the total transfer.
Virtual Node
One of one or more nodes co-resident within a single board or computer. Often a board is a single node, but it's possible for a board or computer to behave on the OpenLCB as if it contained multiple nodes. Those are then referred to as virtual nodes.
Well Known Events
Certain Events are globally defined to have specific meanings. Their Event IDs are documented as part of the event protocol. These are called “well known events”.
Wire protocol
Version of the OpenLCB common messages, interactions, etc adapted to a particular transport mechanism. Examples are the wire protocols for CAN bus segments and TCP/IP links.
# CAN Glossary
CAN
Controller Area Network, an ISO-standardized communication network type. The CAN specification includes aspects of the physical- and link-layer definitions for OpenLCB.
Frame
A Frame is packet as it is defined on the CAN bus. It consists of a 11 or 29 bit CAN header and zero through 8 bytes of data. An OpenLCB message may become one or more frames when transmitted over CAN. Some frames, called Control Frames, are used for link-layer control and do not correspond to any particular OpenLCB message.
OpenLCB-CAN
Short form for “OpenLCB as implemented on a CAN link”. For example, “OpenLCB-CAN message” refers to an OpenLCB message formatted for transmission over a CAN link.
Segment
A single CAN segment is the set of CAN nodes that share CAN arbitration.