# 1. NMRAnet TM Introduction
This document describes NMRAnet, a local control bus developed as a parallel to locomotive control, such as DC and DCC.
# 2. Transports
Although NMRAnet is designed to operate on multiple transports, this document will be limited to descriptions of the protocol adapted to CAN and Ethernet.
CAN Standard Version 2.0 A&B shall be adhered to for all signals on the CAN bus. The CAN Extended frame shall be used by NMRAnet to transfer data.
Ethernet standards are adhered to in the adaptation of NMRAnet to it.
# 3. Common Protocol Frame Definition
The Common protocol describes the generalized protocol that is not directed at a specific transport. The following is the Common Protocol Frame Definition:
<MTI:16><sNID:48>{<dNID:48>}{<Flags:8}<Length:16><Data:0-2k>
Where:
MTI – message type indicator
sNID = source node-ID
dNID = destination node-ID
Length – length of data bytes
Data – data associated with the message
## MTI – Message Type Identifier:
<00110><pri:2><0><type:4><0><DID:1><EV:1><Flags:1>
Where:
<00110> - reserved field, must be checked
<pri:2> - priority, 00 is high, 11 is low
<0> - reserved
<type:4> - type of message
<0> - reserved
<DID:1> - Destination node ID indicator, 0=not present, 1=present
<EID:1> - Event ID indicator, 0=not present, 1=present
<FLAGS:1> - flags-byte indicator, 0=not present, 1=present
Notes:
1. If the DID is present, it must be mappable to the full NID., and is located at the start of the data-part;
2. If the EID is present, it follows the EID, if present, else is located at the start of the data-part;
3. If the flag-byte is present, the low bits of it may be relocated in CAN messages.
## sNID – Source Node ID:
The can be the full node ID (48-bits) or an alias on some transports, such as CAN. It must be translatable between the two forms.
## dNID – Destination Node ID:
This is an optional field, and its presence is indicated by the DID-bit in the MTI.
## Event ID:
This is an optional field, and its presence is indicated by the EID-bit in the MTI.
## Flags-byte:
This is an optional field, and its presence is indicated by the Flags-bit in the MTI.
## Data:
This is an optional field, and can be up to 2k in length.
# 4. Common Protocol
The common Protocol has three basic message types:
- Events: <00110><pri:2><0><xxxx><0010><sNID><event#>
- Datagrams: <00110><pri:2><0><yyyy><0z00><sNID>{<dNID>}<data:0-2k>
- Streams: <00110><pri:2><0><zzzz><0100><sNID><dNID><data:0-2k>
# 5. CAN Protocol
General CAN format: [<header:29>](<length:4>) <data:0-64>
Where:
<header:29> - 29-bit header
<lenght:4> - number of data bytes
<datapart:0-64> - data-bytes, 0-8
## Forms:
[<format:3><0000><type:8><sNIDa>](len:4>)<data:0-8> or
[<format:3><dNIDa:12><sNIDa>](len:4>)<data:0-8>
## Formats:
1. 0 Simple MTI
2. 1 Complex MTIFull source node ID
3. 2 n/u
4. 3 n/u
5. 4 Datagram frame, fragment, continuing
6. 5 Datagram frame, last fragment
7. 6 Destination, non-stream
8. 7 Destination, stream
## Basic Messages:
Events
[<pri><0><0x02D><sNIDa:12>]<8><event:64>
Datagrams
    Middle:
[<pri><4><sNIDa:12><dNIDa:12>](<len:4>)<data:0-64>
    End:
[<pri><5><sNIDa><dNIDa>](<len:4>)<data:8-64>
Streams
[<pri><7><dNIDa:12><sNIDa:12>](<len:4>)<data:0-64>

## Management Messages:
Initialization complete:
[<pri><1><0x008><sNIDa>](6) NID
Verify Node ID Number
[<pri><6><dNIDa><sNIDa>](1) 0x0A – specific node
[<pri><0><0x00A><sNIDa>](0)	- all nodes
Verified Node ID Number
[<pri><1><0x00B><sNIDa>](6) NID
Optional Interaction Rejected
[<pri><6><dNIDa><sNIDa>](2) 0x0C MTI
Terminate Due to Error
[<pri><6><dNIDa><sNIDa>](2) 0x0D MTI
Event Exchange Messages
Identify Consumers
[<pri><0><0x024><sNIDa>](8) EID
Consumer Identify Range
[<pri><1><0x025><sNIDa>](8) Event-mask
Consumer Identified
[<pri><1><0x026><sNIDa>](8) EID
Identify Producers
[<pri><0><0x028><sNIDa>](8) EID
Producer Identify Range
[<pri><1><0x029><sNIDa>](8) Event-mask
Producer Identified
[<pri><1><0x02A><sNIDa>](8) EID
Identify Events
[<pri><6><dNIDa><sNIDa>](1) 0x2B – specific node
[<pri><0><0x02B><sNIDa>](0) - all nodes
Learn Event
[<pri><0><0x02C><sNIDa>](8) EID
P/C Event Report (event message)
[<pri><0><0x02D><sNIDa>](8) EID