Error Codes
Bits	Description
12-15	Error type flags.
8-11	Reserved. Send as zero, ignore on receipt.
4-7	General Error Enumeration 0-15.
0-3	Reserved for use of specific protocols for error reporting. Interpretation of these bits will be defined in the specific protocol documentation. A value of zero in this field means no further information is available.
Value	Description
Permanent Error Enumeration. Re-trying the same interaction will result in the same error.
0x1000	Permanent error, not further specified.
0x1010	Unimplemented, not further specified.
0x1020	Source not permitted.
0x1030	Reserved.
0x1040	Unimplemented, not further specified.
0x1050	Unimplemented, subcommand is unknown.
0x1060	Unimplemented, Datagram-type, Stream-type, or command is unknown.
0x1070	Unimplemented, unknown MTI, or Transport protocol (datagrams/streams) is not supported.
0x1080	Invalid arguments. Some of the values sent in the message fall outside of the expected range, or do not match the expectations of the receiving node.
0x1090-0x10F0	Reserved.
Temporary Error (resent OK). Re-trying the same interaction later is likely to succeed.
0x2000	Temporary error, not further not specified.
0x2010	Reserved.
0x2020	Buffer unavailable or destination node busy.
0x2030	Reserved.
0x2040	Unexpected, Out of order. An inconsistency was found in the message or frame sequence received, the arrived message is unexpected or does not match the state of the receiving node.
0x2050-0x2070	Reserved.
0x2080	Transfer error. The message or received message was ill-formed, failed checksum, or is otherwise uninterpretable. On CAN, this is handled by the hardware.
0x2090-0x20F0	Reserved.
Reserved
0x4000	Reserved. Write as zero, ignored on read.
Accept Flag
0x8000	Accept, no error. This value shall not be used in reject messages.

Examples:

Protocol X might define:
0x0001 – error flag 1
0x0002 – error flag 2
0x0004 – error flag 3
0x0008 – error flag 4
So, a node might send:
    0x1051 unimplemented subcommand, flag 1
or 0x1053 unimplemented subcommand, flag 1 and flag 2

Protocol Y might define:
0x0001 – enumeration 1
0x0002 – enumeration 2
0x0003 – enumeration 3
0x0004 – enumeration 4
So, a node might send:
    0x1051 unimplemented subcommand, reason1
or 0x1054 unimplemented subcommand, reason4