# Introduction (Informative)
This document defines a standard for the storage of static information that describes the user interface options for controlling available functions on an OpenLCB Train Node, called “Function Description Information (FDI)”.
The format is XML-based in order to allow reasonable extensibility, while enabling programmatic generation and parsing of the structured information. This XML document is specific to the particular Train, and is exposed at the Memory Space 0xFA. Throttle Nodes retrieve this data from the Train Node using the Memory Configuration Protocol.
This concept and interaction is using the same pattern and similar format as the Configuration Description Information, purposefully, with the expectation that OpenLCB devices will be able to share the software implementation between these two use-cases.
# Intended Use (Informative)
The most important use-case of operating a model train is controlling speed and functions. The protocol for these are defined in the OpenLCB Train Control protocol Standard. The user typically uses a Throttle for performing these operations, either as a special-purpose hardware device, or as a software function on a generic computing device.
While the semantic meaning of speed control is very well defined, the meaning of functions is left very vague by the OpenLCB standard, just like other standards of the industry; a function is some form of remote controlled feature of the train (or locomotive). This vague definition is intentional, as manufacturers have come up with new and innovative ideas on what kind of additional features they want to add to their models, and the typical way to operate these features is using the function abstraction.
Typical functions are lighting functions (like headlights, tail lights, class marker lights, etc.), motor control functions (momentum, braking, etc.), sound functions (horn, bell, whistle, engine sounds, compressor, etc.) and a variety of other functions, such as a smoke unit, raising and lowering a pantograph or operating a locomotive-mounted remote uncoupler. There is no definitive list of all possible functions, the TN-218 document by RailCommunity lists over 120 different types.
Not only is the list of possibilities is very large, one specific model alone can carry dozens of different functions. Users have to activate these typically by their function number, for example using a numeric keypad. This is easy to operate, provided that the user has memorized which function number does what on that specific locomotive. With dozens of functions per locomotive and up to hundreds of locomotives on a big layout, this is no easy task. As such, it is an important use-case for the Throttle to display a user interface that provides information to the user about what function numbers are available, and which numbers perform what on the train.
The Function Description Information (FDI) provides exactly this metadata for the throttle: the list of functions, for each function what number it is accessible as, and a textual description on what the given function does.
In addition to the description for the user, the throttle user interface needs some additional metadata to determine how theparticular function button should behave. There are two common behaviors for on/off functions: momentary functions are turned on while the user is holding the button, and turned off upon release. Toggle (or binary) functions are turned on with a press of the button, then they stay on after release, until the user presses the button again. A typical momentary function is horn, a typical toggle function is headlight. This is purely a behavior of the user interface, as the underlying protocol for turning the function on and off is the same for both cases.
# References and Context (Normative)
For more information on format and presentation, see:
OpenLCB Common Information Technical Note
# Format (normative)
## Use of XML
## FDI is constant
## Other stuff
The FDI information shall be constant. A node may not change it after any part of it has been retrieved and before the next transition of the node away from the Initialized state. (The transition back to Initialized state tells other nodes to flush their caches and pick up any changed content)
# Stuff to be merged into the above (or the TN)

The first byte is used to distinguish the coding.
“<” (which is part of the XML “<?xml version='1.0'?>” definition): Uncoded characters
UTF BOM: Various UniCode forms
0x01 – tag for compressed. One format defined for total start string of 0x0101. (If you want to use another format, decompress on board)
(can't use 0x00 as lead, since that's the end-of-string indication)