# Introduction (Informative)
This specification describes the format and allocation of OpenLCB 48-bit unique identifiers. It is not specific to any wire protocol.
For more information on format and presentation, see:
OpenLCB Common Information Technical Note
# Intended Use (Informative)
Many OpenLCB protocols rely on each node having a node ID, and those node IDs being absolutely unique between nodes. OpenLCB defines 48-bit unique identifiers for this purpose. Unique identifiers are also used to ensure that Event Identifiers are uniquely specified, and for other purposes. This Standard is intended to ensure these unique IDs are available. It applies to all OpenLCB uses of 48-bit unique identifiers, including as node identifiers.
# References and Context (Normative)
This specification is in the context of the OpenLCB-CAN … Specification, which specifies …
# Format (Normative)
An OpenLCB unique identifier (unique ID) shall be six bytes of eight bits each.
The order of bytes in an OpenLCB unique ID shall be considered significant. The most-significant byte shall be transmitted first during communication operations. The most-significant byte shall be written first (left-most in Western format) in any human-readable representation.
OpenLCB unique IDs shall include one or more 1 bits.
Every OpenLCB node shall have a unique identifier to use as a node identifier.
# Allocation (Normative)
Unique identifiers shall be allocated using one of the mechanisms in this section.

## Node numbers assigned by manufacturers
Manufacturers who have been assigned a manufacturer ID number by the NMRA may, but are not required to, use their NMRA manufacturer ID number to self-assign unique identifier numbers using the pattern:
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x02	0x01	Mfg ID byte	self-assigned	self-assigned	self-assigned

Manufacturers shall ensure that the same node ID is not used by more than one node.
## Node numbers assigned by members of organized groups
A NMRA member may, but is not required to, use their NMRA membership number to self-assign node ID numbers using the pattern:
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x03	0x00	Member Number			Self-assigned

A MERG member may, but is not required to, use their MERG membership number to self-assign node ID numbers using the pattern:
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x03	0x04	Member Number			Self-assigned

Individuals using this assignment pattern shall ensure that the same node ID is not used by more than one node.
## Node numbers assigned by software at run-time
A program running in a computer with global IP address may, but is not required to, use that IP address to self-assign node ID numbers using the pattern:
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x04	IP number	IP number	IP number	IP number	self-assigned

IP addresses in the following ranges shall not be used:
      10.0.0.0 – 10.255.255.255
      172.16.0.0 – 172.31.255.255
      192.168.0.0 – 192.168.255.255
      169.254.0.0 – 169.254.255.255
Programs using this assignment pattern shall ensure that the same node ID is not used by more than one node.
## Node numbers assigned using other's methods for assuring uniqueness
Other groups have defined mechanisms to ensure that node ID numbers or equivalent constructs are uniquely assigned. They may have e.g. non-technical reasons for wishing to use those same mechanisms to assign OpenLCB node IDs. Ranges of OpenLCB NIDs can be assigned to these, so that when people then use the group's mechanism to select a number within that range, the result will be a properly unique NID.
The first example of this is MERG CBUS developers. MERG CBUS has defined a “no cost” way of identifying unique 16-bit Node Number (NN) for CBUS use, perhaps with an option 16-bit “Layout Number”. People who wish to use this mechanism to allocate unique OpenLCB Node ID numbers can, without having to consult anybody, generate an OpenLCB Node ID from the unique CBUS number(s) as follows:
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x03	0x05	Layout High	Layout Low	NN High	NN Low

## Global identification numbers
Well-known global identifiers

Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Use
0x01	1	0x00	0x00	0x00	0x00	Well-known Event IDs
0x01	1	0x01	0x00			CBUS mapped Event IDs
0x01	99					XpressNet translation
0x01	129	Byte 1	Byte 2	Byte 3	Byte 4	LocoNet packet transport
0x01	238					DCC translation

## Assigned for use with locomotive control systems

Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Use
0x06	0					DC (block)
0x06	1					DCC
0x06	2					TMCC
0x06	3					Marklin/Motorola
0x06	4					MTH DCS

## Number ranges assigned by request
Any individual or corporation shall be able to obtain permanent allocations of blocks of 28, 216 and 224 node identification numbers via the http://www.openlcb.org web site.
## Reserved numbers
Node IDs in the following range shall not be used.

Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x00	Any	Any	Any	Any	Any
0xFF	Any	Any	Any	Any	Any

All other node ID numbers not specifically discussed in this Standard shall not be used.