# Introduction
This Technical Note contains informative discussion and background for the corresponding “OpenLCB Unique Identifiers Specification”. This explanation is not normative in any way.
Originally, OpenLCB was written in terms of 48-bit unique “node IDs”. Other uses were found for these IDs that didn't associate them with a specific node, which demonstrated the need for unique IDs beyond just node IDs. Therefore, the Standard and this Technical Note are generally written in terms of unique IDs, which includes use for node IDs.
Note that a node ID must be truly unique, in the sense that it's ID can't be used either for another node nor for any other purpose.
# Annotations to the Specification
This section provides background information on corresponding sections of the Specification document. It's expected that two documents will be read together.
## Introduction
## Intended Use
The "globally unique" requirement only refers to the universe of connected nodes; nodes that never need to communicate with each other need not have separate NIDs. In general, however, nodes can move: They can be sold or loaned for use on another layout, nodes on modular layouts can be connected to other arbitrary modules, and few assumptions can be made. It's best if nodes are given a completely unique ID when manufactured, so there's no need to ever detect and resolve a conflict.

## References and Context
## Format
The specification doesn't require any particular human-readable format, but hex-pairs with separators are strongly suggested, e.g. 01.AB.34.01.CD.E3; decimal pairs could also be used, but in that case it's important to provide a way to know which is use.

Discuss who's responsible for ID uniqueness. “Last constructor”, e.g. person who assembles and configures a kit?
Make it clear that there are many methods to store the ID, and that's not constrained by the Standard.
If the user is involved in determining the Node ID, e.g. by setting switches, the node has to provide a user-visible way to indicating a duplicate has been seen, and must implement the relevant wire-protocol-specific methods for detecting duplicate node IDs.s

## Allocation
Unique IDs are assigned via a delegation process. At the highest level, number ranges are assigned to people and organizations, within which they are responsible for assigning unique numbers to separate devices. These ranges can be subdivided and delegated further, as needed. Additional ranges can then be requested, which will be recorded here or eventually in some online system accessible to anybody.
Anyone may request a block of IDs of a suitable size, which are then automatically assigned. It is preferred that this be an easy process, perhaps just filling out a web form, so that people can rapidly obtain and use unique IDs. For now, all assignments are documented in a web-accessible spreadsheet (.ods) (.pdf).
In addition to ranges directly delegated by the central authority, there are several special-case populations of modules:
1. Numbers assigned by manufacturers
2. Numbers assigned by members of organized groups
3. Numbers assigned by do-it-yourself hobbyists
4. Numbers assigned by software at run-time
One of the reasons for having a long, 48-bit NID space is to make it easier to have alternative approaches like this. Particular assignments for these populations are discussed below. In each table, the blank bytes on the left (most significant bytes) will be assigned fixed values for distinguishing the various types.
In these delegated assignments, the lower order byte(s) are self-assigned. The values of zero is reserved, indicating that a number within the range hasn't been assigned.
### Numbers assigned by manufacturers
As an initial simplification, and to encourage manufacturers to adopt OpenLCB, a group of 2^24 addresses will be assigned to each manufacturer with an NMRA manufacturer ID number. Manufacturers can assign a board any Node ID number from within their range so long as each number is only assigned to at most one node.
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x02	0x01	Mfg ID byte	self-assigned	self-assigned	self-assigned

The NMRA has defined ID number 238 for future expansion with in the existing 8-bit ID space, but has not determined how to use it. When 238 is finally used to identify a new set of manufacturers, those manufacturers can be assigned OpenLCB ranges with a different set of high-order bits.
Software manufacturers who use software keys can generate the low-order 24 bits from some unique part of the software key. Hardware manufacturers need to ensure that resetting a device to “factory defaults” doesn't lose the self-assigned part of the Node ID, e.g. the serial number.
### Numbers assigned by members of organized groups
MERG kit builders and others would like to assign their own numbers without going through a complicated process. To make this possible without any interaction with anybody, these people are assigned number ranges that involve their member number in the organization. A member may assign any number from this range to the node(s) they produce, provided that each number is assigned to at most one node. A range of 255 numbers per member is sufficient for hobby usage; after building that many, the hobbyist can get another, larger assignment. It's also convenient to give hobbyists a byte as their range.
Each organization is assigned a unique high-order two bytes. The organization member number is given 24 bits.
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
		member number	member number	member number	Self-assigned

Specific leading bytes are documented in the spreadsheet (.ods) (.pdf), but the first two assignments are:
Byte 1	Byte 2	Group
0x03	0x01	NMRA
0x03	0x02	MERG

### Numbers assigned by software at run-time
Programs that act as one or more OpenLCB nodes need to associate unique NIDs with them. For licensed software, where a unique key can be associated with each instance of the program, this is easy: Use the manufacturer space defined above, and generate the lower bits of specific ID from the license key.
Free, open and unlicensed software can't use a license-key-based method. Unfortunately, the 48-bit address space is too small to use the IP-address-plus-signature GIDs that would otherwise make this a simple problem, or the even larger MAC-address-plus-signature GIDs.
If the computer has a global IP address (not part of one of the four non-global IP ranges), that can be used initially.
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x04	IP number	IP number	IP number	IP number	self-assigned

Non-global IP addresses (see appendix) will require another algorithm. It may be as simple as requesting that the user get a number from one of the above spaces and provide it. If the software determines it has an internet connection, it could also request a unique allocation from a central source.
Use of time in nsec from some epoch; needs a prefix for e.g. manufacturer number in case of multiple programs coming up at some time? (You expect a collisions in nsec? Seriously?)
There are three ranges of IP addresses that are "private":

10.0.0.0 - 10.255.255.255 (2^24 addresses)
172.16.0.0 - 172.31.255.255 (2^16 addresses)
192.168.0.0 - 192.168.255.255 (2^16 addresses)

In addition, a range is reserved for the Windows
"Automatic Private IP Addressing" feature:
169.254.0.0 -169.254.255.255 (2^16 addresses)

The A/B/C class system:
A has 0XXX,XXXX in 1st octet (0-127) and allocates 24-bit ranges
B has 10XX,XXXX in 1st octet (128-191) and allocates 16-bit ranges
C has 110X,XXXX in 1st octet (192-223) and allocates 8-bit ranges
D has 111X,XXXX in 1st octet (224-255) and is used for multicast, etc.

But the regularity this defines is used for routing, something not needed in the much smaller OpenLCB network.

EUI-48 addresses (used to be known as MAC addresses) are 46 bits (48, but two of them indicate global/local and other use).
### Numbers assigned using other's methods for assuring uniqueness
Other groups have defined mechanisms to ensure that node ID numbers or equivalent constructs are uniquely assigned. They may have e.g. non-technical reasons for wishing to use those same mechanisms to assign OpenLCB node IDs. Ranges of OpenLCB NIDs can be assigned to these, so that when people then use the group's mechanism to select a number within that range, the result will be a properly unique NID.
The first example of this is MERG CBUS developers. MERG CBUS has defined a “no cost” way of identifying unique 16-bit Node Number (NN) for CBUS use, perhaps with an option 16-bit “Layout Number”. People who wish to use this mechanism to allocate unique OpenLCB Node ID numbers can, without having to consult anybody, generate an OpenLCB Node ID from the unique CBUS number(s) as follows:
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x03	0x05	Layout High	Layout Low	NN High	NN Low

### Number ranges assigned by request
### Reserved numbers
For error detection and future expansion, we reserve all numbers that start with either a 0x00 or 0xFF value.
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x00	Any	Any	Any	Any	Any
0xFF	Any	Any	Any	Any	Any

Node numbers starting with 0x00 can be used on a temporary basis for experimentation. In particular, an experimenter can use numbers in that range as a starting point, and then assign more permanent numbers before distributing nodes to others or using them in combination with nodes from others.