# Introduction
This Technical Note provides background information and commentary to the OpenLCB Train Search Protocol Standard (in short ‘the Standard’). This document is not intended to be read standalone, but in parallel to the Standard.
When we use capitalized terms Train, Throttle, and Command Station, we refer to the definitions according to the Section ‘Interactions’ in the Standard.
## Background
### Relation to Traction Protocol
The OpenLCB Network is a peer-to-peer network where Nodes connected to the network can communicate with each other using the OpenLCB Network Protocols. These protocols are organized around the different OSI layers, and to achieve an end-to-end use-case a multitude of protocols are typically used, from different layers[1], or in a complementary manner[2].
[1] Example: The Memory Configuration Protocol is using the Datagram Protocol as a supporting layer.
[2] Example: for end users to configure an OpenLCB Node, the Memory Configuration Protocol is expanded with the Configuration Description Information protocol to describe what configuration settings are available at which memory offsets.
Some of these protocols are broadcast, meaning that all Nodes receive the messages of the interaction; other protocols are addressed, meaning the interaction takes place between two specific Nodes, and other Nodes do not receive the messages of the interaction. In order for an addressed interaction to take place, the initiating Node needs to know the Node ID of the target Node. This generally requires some broadcast protocol using which the initiating Node can discover the possible target Nodes, and present these on a user interface to the user to select.
Considering the interaction of a user using an OpenLCB-connected Throttle to communicate to an OpenLCB-connected Train, or an OpenLCB-connected Command Station, we have two protocols that are part of this interaction:
- The Traction Protocol defines the addressed interactions related to driving a train, such as setting speed and direction, or operating functions. It takes place between one Throttle and one or more Train Node(s) that are controlled.
- The Train Search Protocol is a broadcast protocol that specifies interactions needed for the Throttle to identify the Node ID of the Train Node that the user intends to drive.
### Relation to Legacy Track Protocols
Trains may or may not be equipped with the necessary technology to directly participate in the OpenLCB Network. For now and the foreseeable future, an overwhelming majority of digitally controlled trains will be using a mobile decoder that operates using an existing standard or proprietary method of transmitting commands to the mobile decoder through the track, such as the NMRA® DCC® protocol suite.
In such a setting, there is a centralized component called Command Station which is responsible for generating the track protocol signal. This device has to receive commands from the Throttles, and translate them to remote control the mobile decoders built into the trains rolling on the track. The Command Station is then responsible for participating on the OpenLCB Network and representing the remote trains. The Traction Protocol requires each train to be a separate OpenLCB Node with its own Node ID, therefore the one Command Station device will be operating a number of Virtual Nodes, one per actively controlled train. All of these Virtual Train Nodes participate in the Train Search Protocol so that Throttles can discover, find and operate the trains connected to the track.
An important question then becomes: how does the Command Station know when the user intends to address a new train on the track that does not yet have a matching Virtual Train Node. The Train Search Protocol addresses this use-case as well.
### Relation to other Search and Discovery Protocols
Note that the existence of Train Search Protocol does not exclude other methods and standards, including some not yet developed, for the same or similar purposes. There are also possibilities of using less capable existing Standards to achieve similar results (covering some but not all use-cases), albeit at a higher cost for the Throttle Node in terms of the necessary resources (above all RAM) and higher number of network messages to send and keep track of.
Some of these options are described in the Alternatives Considered section below (TODO: replace with reference).
## Served Use Cases
- The User is holding a Throttle connected to the OpenLCB Network. The Throttle has a numeric keypad and no screen. The user types in the four digit cab number they see on the locomotive and presses the Enter key. The Throttle uses the Train Search Protocol to find the matching OpenLCB Node. Then the throttle uses the Traction Protocol to connect to that Train Node, and the user is able to drive the train.
  Note that this use-case presents the same way if the train itself has a radio-equipped decoder and is directly participating on the OpenLCB network; and also if the train has a DCC decoder and represented by a Command Station on the OpenLCB Network.
- The user owns a locomotive with road number 474 014 with a legacy track protocol decoder. The user does not remember what address is assigned to the decoder, but there is a Roster (locomotive database) in the Command Station, which has a record of the track address, and the name “Re 474 014” is assigned to this record. The user has a Throttle with a numeric keypad and a screen, and types in 474 on the keypad. The Throttle uses the Train Search Protocol to look for matching entries on the network. The Command Station searches through the Roster, instantiates the matching Virtual Nodes, provides the list of matching Node IDs to the Throttle. The Throttle queries the user-visible names of those Nodes using the Simple Node Information Protocol and presents a list to the user to select from. The user selects “Re 474 014”, and starts driving the train.
- The user purchased a new locomotive which came with a Marklin-Motorola format mobile decoder with address 72. The user puts it onto the track, types in 72 on the throttle, selects the Marklin-Motorola track protocol using option keys, and presses Enter. The user is in control of the locomotive.
- A friend comes over and brings a DCC-equipped locomotive with them. They warn that the locomotive has a very old decoder. The user enters the address on the Throttle, selects the DCC-14-speed-step protocol using option keys, and presses Enter. The user is in control of the locomotive.
- A Gateway device connects a proprietary layout control bus to OpenLCB. Throttles connected to the proprietary bus select locomotives by a DCC address. The Gateway device intercepts these messages and sends out Train Search Protocol messages to the OpenLCB bus. A DCC Command Station connected to the OpenLCB bus creates Virtual Train Nodes for the intended locomotives. A radio-equipped OpenLCB locomotive that has an up to 4 digit number on the cab can also be selected using this method.
- A large software system designed to control model railroads has a system-specific implementation module for a variety of different command systems. The API of this module gives a 4-digit DCC address to select a locomotive. The OpenLCB implementation of this API translates this number to a Train Search Protocol message in order to trigger an OpenLCB-connected Command Station to create a Virtual Node. The Command Station uses its settings to decide whether it should be a DCC protocol train or some other protocol (e.g. Marklin-Motorola). A radio-equipped OpenLCB locomotive that has an up to 4 digit number on the cab can also be selected using this method.
## Unserved Use Cases
- The Train Search protocol is not a generic search protocol. It is not possible to search for any other entity than a Node[3]. While the concept could be used for searching for other types of nodes, the specific allocation shall only be used for searching for Train Nodes. This is necessary in order to ensure that Throttles that use this allocation properly function on the network.
  [3] For example it is not possible to search for an Event.
- The search results are only Node IDs. If additional information beyond the Node ID is needed (such as user-visible name), the Throttle has to use other protocols (such as the Simple Node Identification Protocol) to query that information.
- Only digits are supported in the search query. The maximum length of the query is 6 digits. Longer and alphanumeric search queries are not supported.
- A Command Station can only receive a signal using the Train Search Protocol when the user wants a new Virtual Train Node to be created. The Train Search Protocol does not support giving a signal to the Command Station on when to delete a Virtual Train Node.
## Overview of the Protocol
The Train Search Protocol is fundamentally a broadcast search protocol in a peer-to-peer network. The Throttle broadcasts the search query, which reaches all other Nodes; the matching Nodes reply with a broadcast message which reaches the Throttle, allowing the Throttle to compile a list of results.
The input from the Throttle side is a number with up to 6 digits. This number is encoded using BCD into 3 bytes. An additional flag byte is appended that describes options related to protocol to be used (e.g. DCC with 128-speed-step) and specifies certain behavioral parameters for what Train Nodes should report a match. A fixed 4-byte prefix is prepended, which yields an Event ID.
The Throttle sends out an Identify Producer (broadcast) message to the bus. This broadcast message will reach all segments where there is a Command Station or a native OpenLCB Train Node[4].
[4] Command Stations and Train Nodes shall declare themselves by sending a Producer Range Identified message upon startup that covers the entire range of the Train Search Protocol Event IDs.
Train Nodes (both OpenLCB-connected and Command Station managed), upon receipt of such Identify Producer command, will evaluate the request against their identifying properties (e.g. address, cab number, Node name). If they find that the request matches their identifying properties, the Node responds with a Producer Identified message on the same Event ID. If the request does not match that node, no Producer Identified message is emitted.
If no response arrives for 200 msec, and the request specifies so, then a Command Station will create a new Virtual Train Node matching the parameters in the request. The new Node will then emit a Producer Identified message to the bus.
The Throttle is waiting for Producer Identified messages on their requested Event ID. These messages contain a Source Node ID (or equivalent representation). These are the search results. The Throttle may pick the first search result’s Node ID and operate that train using the Traction Protocol, or if multiple responses arrive, then the Throttle may interrogate those Nodes using the SNIP and PIP protocol to present a list of possible trains to select to the user, if there is a display.
# Annotations to the Standard
The Subsections herein mirror the structure of the Train Search Protocol Standard document.
## Introduction
Note that this section of the Standard is informative, not normative.
The Train Search Protocol is built on top of the Event Transport Protocol, which operates using generic OpenLCB messages. This means that the Train Search Protocol can operate on any supported OpenLCB transport layer, including CAN-bus and TCP. This allows both wired and wireless Throttles to operate using the Train Search Protocol.
## Intended Use
Note that this section of the Standard is informative, not normative.
## References and Context
There is no reference to the Traction Protocol, which the Throttle would use to drive actual trains. This is on purpose, because the scope of the Train Search Protocol ends after the Throttle discovers the Node ID. The scope of the Traction Protocol begins once a Node ID is known.
## Message Formats
This Standard is built on top of the Event Transport Standard. All of the necessary messages to operate this protocol are allocated and defined in that Standard.
## Allocation
### Identifier Range allocation and License terms
The Train Search Protocol was developed for and proposed as a Standard by Train Control Systems, Inc. It is a valid use of the Unique Identifiers allocated to any specific party for that party to develop proprietary protocols for operating on the OpenLCB network. It is also valid for this party to offer the developed protocol with appropriate documentation as a proposed Standard.
The licensing terms attached to the Standard allows anyone to create compatible products without any concerns related to license fees. It is not permissible however to create an incompatible product.
### Identifier Format
This section only defines what the individual bits and bytes of the given identifiers are allocated to. It is described in the Section ‘Interactions’ how the different parties should be using those fields and identifiers.
Notes about the symbols used in the Track Protocol table:
- 0b10 is a binary number of size 2 bits. The MSB is 1, the LSB is 0.
- The symbol " signals a repeat of the previous row’s value in this column.
- The symbol * signals that the row applies to all possible values in this field.
## Interactions
This section contains a glossary of terms used in the description of the interactions. These terms are used throughout the entire Standard and Technical Note according to these definitions.
Examples:
- A Train Node could be a WiFi-connected decoder built into a model locomotive, which establishes a connection to and participates in the OpenLCB Network. Alternatively, it could be a Virtual Train Node represented by a DCC Command Station for the purpose of the OpenLCB bus.
- The Command Station might be a DCC Command Station, creating the track signal. It could also be a Gateway from OpenLCB to a proprietary bus, remote controlling a Command Station connected to that proprietary bus.
Examples for Train Node properties:
- The Name might be
  - “Re 474 014-5” for a Swiss electric locomotive of the series 474;
  - “BR18 313” for a German steam engine of the series 18;
  - “C&NW F7A 415” for an F7 unit of the Chicago&Northwestern Railroad.
  - “Thomas the Tank Engine”.
- Protocol: DCC 7-bit address; DCC 14-bit address; Marklin-Motorola; MFX/M4; OpenLCB.
- Protocol Version: DCC has three different speed step modes (14, 28, 128 speed step mode). Marklin-Motorola has multiple versions.
- Address: 1 to 127 for DCC 7-bit, 0 to 10239 for DCC 14-bit, 1 to 80 (or 255) for Marklin-Motorola. There is no address for OpenLCB and for MFX/M4, because for these protocols the user is not required to configure a unique numeric value for each decoder. The manufacturer-assigned unique addresses are not relevant for the user and we should not expect the user to be aware of or ever input those addresses by the number. It might be beneficial for an OpenLCB-connected mobile decoder to allow the user to configure a purely numeric cab number, which the Train Node may apply as if it was a DCC address. This can enable a DCC-only throttle to select that OpenLCB locomotive instead of a DCC locomotive of that address. The user has to be aware that such an option makes that specific DCC address unavailable, as the Command Station will never instantiate a Virtual Train Node for that address so long as the OpenLCB locomotive is on the network.
### Search for existing train nodes
On this diagram we see two interactions with the Train Search Protocol.
In the first interaction the user enters some digits, and the Throttle sends this out as a prefix search for trains starting with “47”. There are multiple replies coming back.
In the second interaction the user presses ENTER, and the Throttle sets the “Exact” bit in the flags byte of the request. Only one reply is generated.
It is of critical importance that the Train Nodes use the exact same Event ID in the replies as what came in the request from the Throttle. This is necessary for the Throttle to identify which of the broadcast responses are requested from the particular throttle. If multiple Throttles are operating the Train Search Protocol simultaneously, the Event ID ensures that there is no race condition between the interactions.
This is depicted in the following diagram:
Depending on the packet queuing behavior of the individual Nodes in this interaction the exact sequence might be slightly different. On CAN-bus, the Producer Identified replies have a higher priority than any potential additional request that might be coming in; as such, the replies for the first request will typically precede the second incoming request on the bus. This ensures that Train Nodes and Command Stations do not need an unbounded amount of buffer to handle Train Search Protocol.
### Allocate a new Train Node

On this diagram we see the same two interactions as in Section 2.6.1, where the DCC 47 node does not exist at the beginning of the interaction. The Throttle is configured to send the request with the “Allocate” bit set when the user pressed ENTER. The Command Station waits for 200 msec for any responses to come in to the exact match request, after which it assigns an empty Train Node to proxy for DCC Address 47. The newly started node then responds to the Throttle.
If the low five bits of the flag byte contain a protocol selection information, then the Command Station would create the new Virtual Train Node according to that protocol. Here the CS used the default settings (DCC protocol).
### Event Identifier matching algorithm
In this section a complex logic expression is defined. The parentheses are important in such an expression and they are represented by typographical levels of hierarchies:
- A bullet point list is interpreted to have an open parentheses before the first bullet and a close parentheses after the last bullet.
- Each bulleted line has an open parentheses at the beginning of the line and a close parentheses before the operator at the end of the line.
This logic expression defines the exact interpretation of the various flag bits and query nibbles which were allocated in the Section ‘Allocations’.
It is important that this algorithm is part of the Standard, therefore Command Stations and Train Nodes must follow it very precisely. The interoperability of throttle features and use-cases of mixing Command Station and OpenLCB Train Nodes on the same network depends on the correct implementation of this algorithm.
The following non-normative statements help in interpreting the algorithm. We say that the request is accepted to generate a response, or dropped to not generate a response.
- If the request specifies an unknown (reserved) option, protocol or nibble in the query, the request is dropped.
- The request may or may not specify a Protocol. If there is no Protocol specified (five LSB bits are all zero), then a Train Node with any protocol is eligible to accept. As an example, if the request specifies OpenLCB as protocol, then the Train Nodes maintained by Command Stations for DCC trains will not reply.
- If the Address-Only bit is set in the flags, the match of the numeric part of the request shall only be checked against the Address of the Train Node; otherwise both the Address and the Name properties shall be checked.
- If there is more than one separate sequence of digits in the qq qq qq nibbles, then Address will not match. In this case it’s hard to interpret what numerical value we should assign to this query. Typical throttles with numeric keypad will only ever send a single digit sequence.
- An Exact match against the address is if the numerical value matches the Address’s numerical value. This is the only acceptable match is the Exact-Only bit is set in the flags. If this bit is clear, we also check for prefix match, for example ‘83’ will prefix-match ‘8300’.
- DCC has two overlapping address ranges. Address values over 128 are always interpreted as DCC long addresses. Address values 0-127 are interpreted as either short or long addresses when doing a default search (i.e., match both short and long addresses). The Throttle may specify the protocol to be DCC and set the bit DCC Force Long Address to indicate that a long address train is requested. A common practice for throttles is to select DCC Long Address when the user prefixes the number with an extra zero, e.g. the user typing “053” would be sent as DCC-force-long-address 53, with the Event ID <prefix>53FFFFEC (Note[5]). When the Command Station receives a request with Force Long Address, only the trains with actual long addresses will match. When the Protocol is Default/Any or Protocol is DCC but the Force Long Address bit is clear, we look at the Allocate bit to decide what to do. If the Allocate bit is clear, we match both short and long address Trains. When the Allocate bit is set, we only match short address Trains. This special case is necessary to be able to allocate a DCC train short-address-53 when there is already a DCC train with long-address-53 on the network.

  Some specific examples for this rule:
  [5] This Event ID also sets Allocate, Exact and Address-only bits to ensure that it connects to a DCC train via a Command Station.
  - request “53”, not force long, not allocate => Train 053L accepts, Train 53S accepts;
  - request “53”, force long => Train 053L accepts, Train 53S drops;
  - request “53”, not force long, allocate => Train 053L drops, Train 53S accepts.
- To match a number against the Name of the Train, we look for digits in the Name. When we have a substring of digits in the Name, we start matching the throttle’s digits at the beginning of this substring to get a prefix match. If Exact-Only match is requested, then the substring in the Name has to be exhausted by the throttle’s digits. For example the Name of “C&NW F7A 415” is exact-matched by the query 415, prefix-matched by the query 41 or 4. The query 15 or 5 does not match this name. The query 7 is also exact-matched, because “7” inside “F7A” fulfills the requirement that there are no further digits before and no further digits after. This Name also matches the query nibbles 7F415F, because both terms in the query (“7” and “415”) match the Name.
### Search Result Differentiation
Some possible methods for this differentiation are as follows:
- An exact match might be rated at a higher quality than a non-exact match. This differentiation is shown in the message diagrams in this Section.
- A Command Station may collect statistics about usage of individual addresses. A train that is more recently used could be marked with a higher quality than one that was used a long time ago.
- From the same statistics, a train that is more frequently used might be marked with higher quality than a train that is less frequently used.
Throttles are not required to make use of the differentiated answers. A possible use-case might be as follows:
A throttle with a UI might show a list of Nodes that replied, and this list might be sorted to show better matches ahead of others.
# Alternatives considered
- A more generic protocol could be developed for searching for Nodes on the network; this may be peer-to-peer or based on a centralized database built and maintained by a single Node that stores details about all Nodes available on the network (including all Train Nodes).

  At the time of this writing, no specific proposals exist for this protocol. The requirements space and ambiguity in this domain is very large, and initial discussions in the OpenLCB Group have not sufficed to identify a straightforward solution to this problem.
- All Nodes can be enumerated by the unaddressed Verify Node ID Global message. There is no throttling mechanism provisioned to maintain the list of replies with a limited amount of memory. The Node list can then be further processed using Protocol Support Inquiry (PIP) messages to restrict to Train Nodes and Simple Node Information Request (SNIP) messages for querying identifying properties such as train name.

  Without a throttling mechanism, using this method to find and identify Train Nodes would require an unbounded amount of memory for the Throttle Nodes. This makes it difficult to build simple and cost efficient Throttles.
- All Train Nodes can be identified using the Well-Known Event ID IsTrain. There is no throttling mechanism provisioned to maintain the list of replies with a limited amount of memory.

  Without a throttling mechanism, using this method to find and identify Train Nodes would require an unbounded amount of memory for the Throttle Nodes. This makes it difficult to build simple and cost efficient Throttles.
- A legacy track protocol Command Station could expose a command interface either via dedicated OpenLCB messages or via a Datagram-based protocol to maintain its list of virtual Train Nodes. This protocol could also be out-of-band, for example through a user interface (physical or HTTP-based), or could be coupled to a persistent database using the Memory Configuration Protocol and the Configuration Descriptor (CDI) XML to expose the user interface via a Configuration Tool.

  There was an actual protocol proposal developed for this alternative under the name of Traction Proxy Protocol. The difficulty with this approach is that a Throttle can be programmed to operate using the Traction Proxy Protocol, which would make the Throttle work well with a Command Station, but naturally exclude the ability of this Throttle to connect to native OpenLCB Train Nodes. This makes the solution not desirable as a long-term offering, as it does not provide a seamless upgrade path to radio-equipped locomotives.
- Instead of encoding the information to transmit in Event IDs, a protocol could be developed using custom OpenLCB messages that are marked as global/broadcast in the MTI. This would allow fewer compromises around the encoding.

  Creating a new broadcast protocol would pose difficult questions around buffering and traffic routing. The Event Transport Standard has specific preparation about interconnecting different network segments with filtering and routing for example. All of these features would need to be specifically duplicated to reach similar performance characteristics as using Events. The duplicate features would then have to be specifically implemented by all gateways and routers.

  Even with a protocol defining custom messages, there would be a fairly strict limit on the amount of payload bytes that can be transported. This is because there is no generic protocol layer for transporting broadcast messages on CAN-bus with more than 8 bytes of payload.
# Test Vectors
Query	|---Train Node Properties---|
Result	Event ID	Addr	Name	Protocol
no match[6]	090099FFFFFF1300	45	"FooBar"	DCC
[6] Neither Name or Address matches here.
no match[7]	090099FFFFFF1300	4513	"FooBar"	DCC
[7] Address contains 13 but not as a prefix, therefore it does not match.
   match[8]	090099FFFFFF1300	45	"FooBar13"	DCC
[8] Name contains a sequence of digits matching 13.
   match[9]	090099FFFFFF1300	45	"FooBar135"	DCC
[9] Name contains a sequence of digits which has a prefix of 13.
no match[10]	090099FFFFFF1340	45	"FooBar135"	DCC
[10] Exact match fails in the name.
   match	090099FFFFFF1340	45	"FooBar13 5"	DCC
   match[11]	090099FFFFFF1300	13	"FooBar777"	DCC 128-speed
[11] Address matches here.
   match	090099FFFFF0130C	13	"FooBar777"	DCC long address
no match[12]	090099FFFFF0130C	13	"FooBar777"	DCC 28-speed
[12] This match fails because the request specifies DCC long address, but the train has DCC short address.
no match	090099FFFFF013EC	13	"FooBar777"	DCC
no match	090099FFFFF0130C	13	"FooBar777"	DCC 28-speed
no match	090099FFFFF013EC	13	"FooBar777"	DCC

no match[13]	090099FFFFF13FE6	13	"FooBar777"	DCC
[13] The request specifies a Marklin-Motorola address, but the train is DCC.
   match	090099FFFFF13FE6	13	"FooBar777"	Marklin-Motorola II
   match	090099FFFFF0130C	13	"FooBar777"	DCC 14-speed long address

no match	090099FFFFFF13E0	13	"013"	DCC 28-speed long address
no match	090099FFFFF013EC	13	"13"	DCC 28-speed
[ OK ] MatchTest.longtoshortmatch (0 ms)
[ RUN ] MatchTest.marklinmatch
no match	090099FFFFF13FE6	13	"013L"	DCC 28-speed long address
2
no match	090099FFFFF13FE6	13	"13S"	DCC 28-speed
   match	090099FFFFF13FE6	13	"13m"	Marklin-Motorola I
   match	090099FFFFF13FE6	13	"13M"	Marklin-Motorola II
exact match failed due to mode: desired 1 actual 3
no match	090099FFFFFF13E0	13	"13m"	Marklin-Motorola I
exact match failed due to mode: desired 1 actual 3
no match	090099FFFFFF13E0	13	"13M"	Marklin-Motorola II
   match	090099FFFFFF13E0	13	"13m"	Marklin-Motorola I
   match	090099FFFFFF13E0	13	"13M"	Marklin-Motorola II
no match	090099FFFFF013EC	13	"13m"	Marklin-Motorola I
no match	090099FFFFF013EC	13	"13M"	Marklin-Motorola II
no match	090099FFFFF13FEC	13	"13M"	Marklin-Motorola II
no match	090099FFFFF13FEC	13	"13m"	Marklin-Motorola I
no match	090099FFFFF13FE8	13	"13m"	Marklin-Motorola I
no match	090099FFFFF13FE8	13	"13M"	Marklin-Motorola II
# Recommended Operation
TODO: describe what kind of throttles should be setting what bits in the request.
Use cases to cover:
- dumb throttle with 0-9+ENTER and no screen
- smart throttle with 0-9+enter+screen+scroll
- gateway with four-digit address
- gateway with four-digit address + is_long boolean.

Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.