# Introduction (Informative)
This specification describes the protocol for transporting OpenLCB datagrams via CAN segments.
# Intended Use (Informative)
# References and Context (Normative)
This specification is in the context of the following OpenLCB-CAN Specifications:
The OpenLCB Frame Transport Standard, which specifies …
The OpenLCB Message Network Standard, which specifies …
The OpenLCB Node Identifier Standard, which specifies …
“CAN” refers to the electrical and protocol specifications as defined in ISO 11898-1:2003 and ISO 11898-2:2003 and their successors.
External certification of parts shall be accepted for conformance to these standards. Conformance with a later version of a standard shall be accepted as conformance with the referenced versions.
# Message Formats (Normative)
## Datagram Content
Name	Dest ID	Event ID	Common / MTI	CAN format	Data Content
Datagram Content	Y	N	0x1C48	N/A	0-72 bytes

### CAN-Datagram Content Single Frame

Name	Dest ID	Event ID	Common / MTI	CAN format	Data Content
Datagram Content Single Frame	N	Y	N/A	0x1Add,dsss	0-8 bytes

### CAN-Datagram Content First Frame
Name	Dest ID	Event ID	Common / MTI	CAN format	Data Content
Datagram Content First Frame	Y	N	N/A	0x1Bdd,dsss	0-8 bytes

### CAN-Datagram Content Middle Frame
Name	Dest ID	Event ID	Common / MTI	CAN format	Data Content
Datagram Content Middle Frame	Y	N	N/A	0x1Cdd,dsss	0-8 bytes

### CAN Datagram Content Last Frame
Name	Dest ID	Event ID	Common / MTI	CAN format	Data Content
Datagram Content Last Frame	Y	N	N/A	0x1Ddd,dsss	0-8 bytes

## Datagram Received OK

Name	Dest ID	Event ID	Common / MTI	CAN format	Data Content
Datagram Received OK	Y	N	0x0A28	0x19A4,8sss fddd

## Datagram Rejected
Name	Dest ID	Event ID	Common / MTI	CAN format	Data Content
Datagram Rejected	Y	N	0x0A48	0x19A4,8sss fddd	Error Code

Nodes must accept and process Datagram Rejected messages that do not contain a full data code. Missing error code bits are to be interpreted as zero.
### Error Codes
Permanent errors
Temporary error

DATAGRAM_REJECTED 0x0000
 DATAGRAM_REJECTED_PERMANENT_ERROR 0x1000
 DATAGRAM_REJECTED_INFORMATION_LOGGED 0x1010
 DATAGRAM_REJECTED_SOURCE_NOT_PERMITTED 0x1020

 DATAGRAM_REJECTED_DATAGRAMS_NOT_ACCEPTED 0x1040
 DATAGRAM_REJECTED_BUFFER_FULL 0x2000
 DATAGRAM_REJECTED_OUT_OF_ORDER 0x6000
 DATAGRAM_REJECTED_NO_RESEND_MASK 0x1000
DATAGRAM_REJECTED_RESEND_MASK 0x2000
DATAGRAM_REJECTED_TRANSPORT_ERROR_MASK 0x4000
# States (Normative)
The common OpenLCB datagram protocol has no formal states.
A node implementing the OpenLCB-CAN protocol must maintain a Datagram-started state for each datagram that it is receiving as a sequence of frames. If the node receives multiple overlapping datagrams, the states must be independent.
# Interactions (Normative)
## Normal Transmission
Normal transmission consists of the transmitting node sending a Datagram Content message to the receiving node, followed by the receiving node sending a Datagram Received OK message to the transmitting node. The receiving node shall send either a Datagram Received OK or Datagram Rejected message.
### CAN Protocol
## Rejected Transmission
After the transmitting node sends a Datagram Content message to the receiving node, the receiving node may send a Datagram Rejected message to the transmitting node. The receiving node shall send either a Datagram Received OK or Datagram Rejected message.
### CAN Protocol