# Introduction (Informative)
This specification defines the protocol for transmitting unidirectional streams of data between two nodes on an OpenLCB bus.
# Intended Use (Informative)
Streaming can be used to move large amounts of data (kilobytes and up) across a OpenLCB implementation. Streaming transport can also be used when the data transfer is unknown or indefinite in its volume or persistence.
# References and Context (Normative)
This specification is in the context of the following OpenLCB Standards:
- The OpenLCB Message Network Standard, which defines the basic messages and how they interact. Higher-level protocols are based on this message network, but are defined elsewhere. The Message Network Standard defines the encoding of stream data message on CAN physical layer, which is referenced here.
- The OpenLCB Memory Access Configuration Protocol Standard, which will be used as an example of an application-level protocol that interacts with the Streaming protocol for data transport.
# Definitions (Normative)
Stream is a uni-directional sequence of bytes transmitted from one OpenLCB node to another OpenLCB node. There is no out-of-band information that can be sent along with the payload using the Streaming protocol. There is no restriction on the total number of bytes sent, or the time that the stream can be open for sending data.
Source node is the OpenLCB node which is sending the data (originating the stream).
Destination node is the OpenLCB node which is receiving the data.
Source Stream ID (SID) is a non-zero one-byte (8-bit) identifier (range [1..255]), assigned by the source node at its discretion to identify the stream.
Destination Stream ID (DID) is a non-zero one-byte (8-bit) identifier (range [1..255]), assigned by the destination node at its discretion to identify the stream.
Stream Content UID is a non-zero 6-byte globally unique identifier assigned to specify the type (format and purpose) of the data being transmitted. Stream Content UIDs are assigned in a similar fashion as Node IDs, but from a different numeric space.
(Max) Buffer size is an unsigned 2-byte value (range [1..65535]) specifying the maximum number of bytes in-flight; that is, the maximum number of bytes the source node may send without receiving a reception acknowledgement from the destination node.
# Message Formats
In the following, the “common MTI” column specifies the MTI value to be used when communicating in OpenLCB common format. The Common MTI is an abstract numeric description intended as a normative guide to the construction of concrete message formats over specific physical transport media.
## Stream Initiate Request
Stream Initiate Request is an addressed message sent by the Source node to the Destination node to request creating the stream. This is the only method to create a stream.
Data content:
Name	Dest ID	Event ID	Common MTI	Data Content
Stream Initiate Request	Y	N	0x0CC8	6 or 12 bytes
				Bytes 0-1	Max Buffer Size (proposed by source)
				Byte 2	Flags: / LSB (bit 0): Type Included 0: No type specification or type specification in Initiate Request message 1: First six bytes of stream payload is the Stream Content UID / bit 1-7: Reserved, send as 0, check on receipt
				Byte 3	Additional Flags: / Reserved, send as 0, ignore on receipt
				Byte 4	Source Stream ID (non-zero)
				Byte 5	Reserved, send as 0, ignore on receipt
				Bytes 6-11	Optional: Stream Content UID, MSB-first

## Stream Initiate Reply
Name	Dest ID	Event ID	Common MTI	Data Content
Stream Initiate Reply	Y	N	0x0868	6 bytes + optional error string
				Bytes 0-1	Max Buffer Size (final value), or zero if the request is rejected.
				Byte 2-3	Error code, or 0x8000 for accept.
				Byte 4	Source Stream ID. Must match the value sent in the Stream Initiate Request.
				Byte 5	Destination Stream ID. May be zero if the request was rejected.
				Byte 6-	(Optional) Error detail string, if rejected.

Error codes are as follows:
0x8000	Accepted
0x4000	Permanent error, specifically
0x4080	Streams not accepted
0x4040	Source not permitted
0x4020	Invalid stream request
0x2000	Temporary error (operation may be re-tried later), specifically
0x2040	Internal error, out of order
0x2020	Buffers full
The following values may be OR-ed to the error code:
0x0001	Information logged. (See the Logging protocol for retrieving logged information.)
0x0100	Stream Content ID included in the stream payload. Must match the “type included” flag in the request.

## Stream Data Send
Name	Dest ID	Event ID	Common MTI	Data Content
Stream Data Send	Y	N	0x1F88	1 – <Max Buffer Size> Bytes
				Byte 0	Source Stream ID / (value = 0, invalid)
				Byte 1 ...

## Stream Data Proceed
Name	Dest ID	Event ID	Common MTI	Data Content
Stream Data Proceed	Y	N	0x0888	2 Bytes
				Byte 0	Source Stream ID / (value = 0, invalid)
				Byte 1	Destination Stream ID / (value = 0, invalid)
				Byte 2	Flags:
				Byte 3	Additional Flags:

## Stream Data Complete
Name	Dest ID	Event ID	Common MTI	Data Content
Stream Data Complete	Y	N	0x0888	4 or 8 Bytes
				Byte 0	Source Stream ID / (value = 0, invalid)
				Byte 1	Destination Stream ID / (value = 0, invalid)
				Byte 2	Flags:
				Byte 3	Additional Flags:
				Bytes 4-7 (optional)	Number of bytes transferred in total, sum of all data segments.

## States
A stream either exists or doesn't; those are states. There are also some un-named intermediate states during setup and take down.
## Interactions
Optionally, the destination can request that the source start a transfer. This uses some mechanism not discussed here, e.g. Datagram messages.
The source sends an "Stream Initiate Request (Addressed)" to the destination. It carries a "Max Buffer Size" value (2 bytes), a “Type Included” boolean flag (1 bit in a byte; see below for meaning) and a "Source Stream ID" (1 byte) in the data section. The combination of source, destination, and Source Stream ID must uniquely identify this stream transmission.
If the destination node does not wish to receive the stream, it returns a "Stream Initiate Reply (Addressed)" marked “reject”, with a "Max Buffer Size" value (2 bytes) of zero, the “Type Included” boolean flag (1 bit in a flag byte), "Source Stream ID" (1 byte) and "Destination Stream ID" (1 byte). The message includes flags set to represent exactly one of several conditions:
“Permanent error” - This node does not process streams, will not accept a stream from this source, or for some other reason will not ever be able to accept this stream. The Stream Initiate Request should not be retransmitted. Optionally, the node can mark the reply with one or more of several conditions:
“Information Logged” - the node supports the logging protocol and information was logged for later retrieval.
“Invalid Stream Request” - something made the stream request improper, such as longer than the max permitted length. Proper requests might be acceptable.
“Source not permitted” - streams from this source will never be accepted
“Streams not accepted” - this node will not accept stream requests under any circumstance. A node can also reject the interaction instead of sending Stream Initiate Reply with this code.
“Buffer shortage, resend” - The node isn't able to receive the stream because of a shortage of buffers. The sending node should resend at its convenience.
“Stream rejected, out of order” - Should not happen, but an internal inconsistency was found in the CAN frames making up a stream. Sender can try again if desired.
If the destination node wishes to receive the stream, it returns a "Stream Initiate Reply (Addressed)" marked “accept”, with a "Max Buffer Size" value (2 bytes), the “Type Included” boolean flag (1 bit in a byte), "Source Stream ID" (1 byte) and "Destination Stream ID" (1 byte).  The "Max Buffer Size" is less than or equal to the value in the Initiate Stream Request, and is the negotiated buffer size for this transfer. If it's zero, the request to start the stream has been rejected, and the exchange is over. The source can try again later. The Source Stream ID is the same as the value in the Initiate Stream Request, and is returned for identification and the convenience of the source. The destination doesn't do anything with it except return it. The source can use it to match up multiple operations, as a way of identifying buffers, or for any other purpose. The Destination Stream ID is used to tag the data sent to the destination. It has no meaning to the source. The destination can, but need not, use it to associate the stream data with a particular buffer or usage. Multiple simultaneous streams can use the same Destination Stream ID value.
The source starts sending bytes using Stream Data Send (Addressed) messages, each carrying up to the message size limit on the particular wire protocol and the Source and Destination Stream ID. After sending exactly Max Buffer Size bytes in one or more messages, the source pauses.
If the “Type Included” flag was true during initialization, the first 6 bytes of the data are a unique data-type indicator. These are allocated the same way that Node IDs, etc, are allocated, but from a separate name space. If that “Type Included” flag is false, some higher-level protocol must identify the data-type of the stream data. The idea is that a stream is a lot of data; there's not much use for one otherwise because of the setup overhead (code and time). So six bytes for a stream type identifier isn't a large cost (unlike e.g. a datagram, where it would be a 10% overhead). A UID as a Stream type ID has the advantage that it's not ever going to collide, so people developing protocols don't have to coordinate it (e.g. useful for future expansion, where a protocol can be locally developed and then deployed more widely). And it still fits in the 1st CAN Frame of the stream, which simplifies what nodes have to do to figure out what type of (unsolicited) data this is. On the other hand, streams have a stream ID, so that a protocol can use some other mechanism (messages, datagrams, or even other streams) to pass the information about what a specific new stream means. That means the type info at the start of the stream isn't as necessary as in e.g. datagrams. (We really wanted to avoid situations like "The next datagram you receive carries the data for this request", because "next" is a hard concept to ensure in code that's doing several things independently)
On CAN, the Stream Data Send message does not carry the Destination Stream ID field. Messages to CAN get split into frames and forwarded without the field. Messages from CAN have to have it inserted by the gateway as part of the translation process. The gateway can do this as part of the (optional) buffer accumulation from frames into larger transfers.
Upon receiving Max Buffer Size bytes via one or more messages, the destination sends a Stream Data Proceed (Addressed) message to the source, carrying the Source Stream ID and Destination Stream ID. This tells the source that there is enough buffer space available that another Max Buffer Size bytes can be sent. The destination can also set flag bits (error codes) in this message to indicate that no more data should be sent and the transmission should be terminated early.
The destination may, but is not required to, send a Stream Data Proceed (Addressed) message to the source before receiving the full count of Max Buffer Size bytes. In that case, the source does not stop transmission after sending Max Buffer Size bytes, but continues for an additional Max Buffer Size bytes of transmission.
When the last data has been sent, the source sends a Stream Data Complete message carrying the Source Stream ID and Destination Stream ID to indicate that all data has been sent. Optionally, this can carry a four-byte length of the stream data transferred for checking. A zero value, if present, means the length is unknown. When this message is received by the destination, the transfer is complete.
# Background Information
## Stream Content Type Identification
Stream senders can, but don't have to, identify the content type (format, meaning, etc) of the data stream at the front. As part of their private protocol, they can use whatever structure they'd like for the data.
General content types can be defined using unique identifiers. The “Type Included” flag identifies that the first eight bytes of stream data are to be interpreted as stream content type information. These can be allocated via the same mechanisms as EventIDs. Well-known ones will be published by OpenLCB. These identifiers are recorded in a separate worksheet.
## Buffer Size
The buffer size can be up to 216-1 bytes = 64KB-1. This is driven by the size of the initiate messages, which we want to keep in a single CAN frame. Although some transport mechanisms might be able to profitably use larger buffers, it seems unlikely that a layout control bus will need to have a higher message efficiency or lower latency than this size will allow. Should that turn out to be necessary in the future, an alternate form for the stream initialization messages can be defined for those large-message nodes. (It's unlikely they're running over CAN)
## CAN Discussion
On a CAN segment, the data limit is 8 bytes. This requires use of as little control information as possible, so that as many of those eight bytes can be used for data as possible.
OpenLCB/S9.6 CAN frames can hold the source and destination aliases in the header. A dedicated “stream data transfer” format can also be coded entirely in the header. This then allows 8 bytes of data per transfer if the Source Stream ID and Destination Stream ID need not be carried. By specifying that only one stream can be transferred on a CAN link between any two nodes at a time, no Stream ID would be needed. Although initially consider, this it thought to be too inflexible. Instead, we chose a format where the Source Stream ID is carried, reducing the payload to seven bytes per frame. This requires that the Source Stream ID be unique among source-destination node pairs, without relying on the Destination Stream ID to be part of the unique stream identification. Since a node knows that it's originating the stream, this can be ensured in advance for point-to-point connections. Gateways will need to track the Destination Stream ID to restore it to the full format. Since they are tracking the stream in any case for buffering purposes, this is thought to be not a large problem.
## Implementation Notes
The "Stream Data Proceed" from the destination is clearance to send another buffer-size-worth of data. To achieve better performance, the destination can send it before receiving the entire buffer-size-worth of data, as soon as it has room to receive what's already been OK'd plus one more buffer size. For example, a destination with a 4kB buffer could reply with Max Buffer Size of 2K, followed by an immediate Stream Data Proceed, to do single overlap of the transfer.
Intermediate nodes need to be able to handle transfers, and therefore need permission to lower the Max Buffer Size on the outbound Stream Initiate Request message. The length in the returned Stream Initiate Reply can't be changed, as the destination need to know when to send clearance for another buffer's worth of data.
A CAN ↔ Ethernet bridge might receive several kilobytes of data from the Ethernet side at a time. It's then responsible for breaking that up into CAN frames and forwarding it. It can reduce the buffer size of transfers if need be to ensure there's a place to store the data while this is done.