# Introduction (Informative)
This specification describes the format and allocation of OpenLCB event identifiers (event IDs). It is not specific to any wire protocol.
# References and Context (Informative)
This specification is in the context of the following OpenLCB Standards:
- The Message Network Standard, which defines the basic messages and how they interact. Higher-level protocols are based on this message network, but are defined elsewhere.
- The Event Transport Standard, which defines the protocol for transporting events.
- The Unique Identifiers Standard witch defines the format and allocation of unique 48-bit identifiers.
# Format
An OpenLCB event identifier shall be eight bytes of eight bits each. Except as specifically noted within this document, the upper 6-bytes are represented by a uniquely assigned Node ID.
The order of bytes in an OpenLCB event ID shall be considered significant. The most-significant byte shall be transmitted first during communication operations. The most-significant byte shall be written first (left-most in Western format) in any human-readable representation.
# Allocation
## Node ID Based
Value					Suffix		Description
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7	Byte 8
6-byte Uniquely Assigned Node ID					**	**	Assigned Node ID event
01	01	01	00	CBUS Node ID		CBUS Event ID		Subset of the assigned Node ID space for CBUS mapped nodes. Node ID is 00 for node short events.

## Well-Known Automatically-Routed
Value					Suffix		Description
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7	Byte 8
01	00	00	00	00	00	FF	FF	Emergency off (de-energize)
				FF	FE	Emergency stop of all operations
				FE	00	Ident button combination pressed
				FD	01	Link error code 1 – the specific meaning is link wire protocol specific
				FD	02	Link error code 2
				FD	03	Link error code 3
				FD	04	Link error code 4

## Well-Known:
The following events identifiers are not automatically routed.
Value					Suffix		Description
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7	Byte 8
01	01	00	00	00	00	02	01	Duplicate Node ID detected
				03	**	Reserved for train Control Protocol
				03	01	Reserved
				03	02	Reserved
				03	03	This node is a Train
				03	04	This node is a Traction Proxy

Below this is just a collection of pieces from other docs right now.