# Introduction
This explanatory note contains informative discussion and background for the corresponding “OpenLCB Event ID Specification”. This explanation is not normative in any way.
# Annotations to the Standard
This section provides background information on corresponding sections of the Standard document. It's expected that two documents will be read together.
## Introduction
Though event identifiers generally take the format of a unique Node ID plus a 16-bit extention, there are some exceptions to this noted in the Event Identifiers Standard which will be detailed in this document.
## Intended Use
An event ID is intended to be globally unique and for a specific purpose defined either by user configuration or enforced by the Event Identifiers Standard. Any node may be configured to produce or consume any event, regardless of its assigned Node ID. However, logically, a unique event identifier is defined to have a unique purpose, whether assigned by user configuration or explicitly defined in the Event Identifier Standard.
## References and Context
This specification is in the context of the following OpenLCB Standards:
- The Message Network Standard, which defines the basic messages and how they interact. Higher-level protocols are based on this message network, but are defined elsewhere.
- The Event Transport Standard, which defines the protocol for transporting events.
- The Unique Identifiers Standard witch defines the format and allocation of unique 48-bit identifiers.
## Format
An event identifier are intended to be globally unique 64-bit values.
## Node ID Based
The majority of event identifiers fall into this category. The 6 most significant bytes are derived from a globally unique 6-by Node ID followed by the two least significant bytes which are typically chosen through user configuration.
### MERG CBUS
OpenLCB allocates a Node ID address space specifically for mapping MERG CBUS events into OpenLCB. CBUS events come in two types: long and short. A long event is uniquely identified by the combination of 16-bit Node ID + 16-bit Event ID. A short event is only identified by its 16-bit Event ID. A CBUS short event is translated into an OpenLCB event by using 0x0000 as the Node ID in the “CBUS Node ID” field of the OpenLCB event identifier. This is allowed because in the CBUS standard, Node ID 0 is not permitted.
CBUS events can also come in the form of a request. These requests should be translated into an Identify Producer on OpenLCB in order to solicit the response that the CBUS request is asking for.
## Well Known Automatically-Routed
Unlike Node ID Based event identifiers, the Well Known Automatically Routed event identifiers are explicitly defined by the Event Identifiers Standard for a specific purpose. Additionally, gateways are required to route these events to all segments.
### Emergency Off
The Emergency Off event identifier (01.00.00.00.00.00.FF.FF) is a request for a node to de-energize all of its outputs. A node receiving this event may continue to remain a powered participant of the OpenLCB bus, but shall de-energize any outputs unrelated to maintaining OpenLCB communications. For example:
- If the node is a DCC power booster, it must disable its amplified DCC power output.
- If the node is an accessory controlling turnout motors, it must remove power from the motors
# (Text to be integrated)
Below this is just a collection of pieces from other docs right now.
The proposed OpenLCB depends on globally unique Event ID numbers (EIDs). This node discusses the assignment of those.
The "globally unique" requirement only refers to the universe of connected nodes; nodes that never need to communicate with each other don't need to have separate Event IDs. In general, however, nodes can move: They can be sold or loaned for use on another layout, nodes on modular layouts can be connected to other arbitrary modules, and few assumptions can be made. Therefore, we require globally uniqueness for all EventIDs.
To ensure uniqueness, the top 6 bytes of EventIDs that you define are required to be within the NodeID space that you control. The low two bytes would be any number you prefer, so long as you use each value for only one event.
This requirement applies equally to events defined by a hardware node, e.g. by button pushing, a software node in a computer, or EventIDs that are defined by a human writing them on a piece of paper. In each case, the thing doing the definition must ensure it has control over the NodeID corresponding to the top four bytes, so it can ensure that the EventID not be reused.
Table 1: Event Number Construction
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7	Byte 8
Node ID assigned to you						Unique 16 bit extension

The Node ID part could be e.g. from real nodes that you own. For example, the Blue/Gold algorithm for assigning Event IDs automatically puts the Node ID of the first node to use that event in the Event ID, guaranteeing it to be unique.
Not all Event IDs need to be assigned through that algorithm. For example, a software configuration tool might define events and assign Event IDs to them. A board manufacturer may prefer some other pushbutton configuration process. A modular club may decide that certain events form the “boundaries” of modules, and need to be assigned well-known Event IDs to make it easier to create large modular layouts. Whatever the method, the Event IDs need to be globally unique, and we ensure that by requiring that people create EventIDs using node ID numbers assigned to them (and therefore not assigned to anybody else), plus an additional 16 bits that they are responsible for using only once.
Note that the Node ID part of an Event ID doesn't have to correspond to any physical node. So long as you've got some Node ID address space assigned to you, you can use that. For example, a fast-clock manufacturer might want to define a range of EventIDs so that a different event is emitted every fast minute. (This lets e.g. lamp controllers do day-night cycles automatically). For the sake of argument, let's say 24 bits worth of specific events are needed (it's actually smaller, but let's use this). The manufacturer has a large range of node IDs assigned already, so can use 8bits worth of that space, plus the extra 16 bits in the EventID below the nodeID-like-part, to do this. For example, if a manufacturer had a range of Node IDs that included at least 0x123456789A00 through 0x123456789AFF (in other words, all possible values of the low byte), he could create a set of Event IDs with the low 24 bits used to carry a time value:
Table 2: Example of defining a Set of Events
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7	Byte 8
Assigned Node ID						Unique 16 bit extension
0x12	0x34	0x56	0x78	0x9A	Time Value

This is guaranteed to be unique, no matter where one of these devices is taken, because the node ID range is guaranteed to belong to the manufacturer, and he'll use it only once.
### Well-known Event ID extensions
Because events are a very convenient way to broadcast information to the entire network, we define some extension values to represent common conditions:

0xFFF8 – Node has logged a new log entry (See logging protocol note)
0xFFF7 -
(But is this mechanism needed? Global events would convey the same information, without using up event space, and the source node ID could be used to determine who said it.
“I've logged an entry”, said Joe Bloggs
“Joe Bloggs has logged an entry”, said Joe Bloggs.