# Introduction (Informative)
A layout control bus can do a number of useful things with fast-time information:
- Connect a number of clock displays to keep them synchronized.
- Provide time displays on plug-in devices, e.g. throttles.
- Provide cueing for time-based occurrences, such as lights turning on and off at specific modeled times.
Generally, existing fast clock systems have one unit that produces time information, here called a clock generator, and one or more units that consume it. It is typically sufficitne to report minutes, not seconds or finer time divisions. Some existing fast clock systems track a day/date in addition to time.
Fast clocks run at various rates, and can be controlled by the user either at the clock generator or from other locations. Some fast clock systems broadcast run/stop and rate information, which can also be useful when interpolating within a fast-minute or between time broadcasting messages.
The OpenLCB protocol presented in this doucment broadcasts time information by producing events with a specific structure of IDs, corresponding to specific times with the day, for example “08:10”. This allows consumers to be taught to react to time-of-day. The year and date are handled separately for those installations that choose to use it.
# Intended Use (Informative)
The primary use of this information is to display time on clock faces around the layout.
Since remote control of the fast clock is desired, a protocol for setting up the time producer using produced and consumed events is defined. This makes it possible for throttles and other nodes with user interface to have a general fast-clock-control capability built in.
In addition, simple nodes can use specific EventIDs to trigger their actions at specific times. For example, lights in buildings in a model town can be sequenced to come on at various times by configuring consumers in a node to react to time events by changing output lines. Most importantly, in this use case, the consuming node does not need to be aware that the event is related to time.
# References and Context (Normative)
This specification is in the context of the following OpenLCB-CAN Standards:
- OpenLCB Event Transport Standard, which defines messages for transporting Event IDs and identifying producers and consumers.
- The OpenLCB Event Identifiers Standard, which defines the format and content of Event IDs including the class of Well-Known Event IDs and Automatically-Routed Event IDs.
- OpenLCB Unique Identifiers Standard, which defines the allocation of OpenLCB 48-bit unique identifiers.
For more information on format and presentation, see:
OpenLCB Common Information Technical Note
# Message Formats (Normative)
This Standard defines a number of Event IDs.

The upper six bytes of the event IDs defined in the following subsections shall be one of the following:
- 01.01.00.00.01.00 – referred to as “Default Fast Clock”
- 01.01.00.00.01.01 – referred to as “Default Real-time Clock”
- 01.01.00.00.01.02 – referred to as “Alternate Clock 1”
- 01.01.00.00.01.03 – referred to as “Alternate Clock 2”
- a valid unique ID under the control of the manufacturer of the clock generator node
- a valid unique ID under the control of the person or organization configuring the clock generator node
The upper six bytes are referred to as the “Specific Upper Part” in the subsections below. In portions of this document, the “Specific Upper Part is also represented by the notation XX.XX.XX.XX.XX.XX.
## Report Time Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						Hours 0x00-0x17	Minutes 0-59

The upper nibble of byte 6 is only 0 or 1, which can be used to distinguish this format.
## Report Date Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						0x20+Month 0x21-0x2C	Day 1-31

The upper nibble of byte 6 is 2, which can be used to distinguish this format.
## Report Year Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						0x3000+Year / 0x3000-0x3FFF

The upper nibble of byte 6 is 3, which can be used to distinguish this format.
The lower twelve bits are the year, 0AD to 4095AD.
## Report Rate Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						0x4000+Rate

The upper nibble of byte 6 is 4, which can be used to distinguish this format.
Rate is a 12 bit signed fixed point rrrrrrrrrr.rr, -511.75, -511.00, …, -1.00, …, -.025, 0.0, 0.25, 0.50, ..., 511.75
## Report Intermediate Time Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						Hours 0x50-0x67	Minutes 0-59

The upper nibble of byte 6 is only 5 or 6, which can be used to distinguish this format.
## Set Time Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						Hours 0x80+97	Minutes 0-59

The upper nibble of byte 6 is only 8 or 9, which can be used to distinguish this format.
## Set Date Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						0xA0+Month 0xA1-0xAC	Day 1-31

The upper nibble of byte 6 is A, which can be used to distinguish this format.
## Set Year Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						0xB000+Year / 0xB000-0xBFFF

The upper nibble of byte 6 is B, which can be used to distinguish this format.
The lower twelve bits are the year, 0AD to 4095AD.
## Set Rate Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						0xC000+Rate

The upper nibble of byte 6 is C, which can be used to distinguish this format.
## Latch Settings Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						0xF000

The upper nibble of byte 6 is F, which can be used to distinguish this format.
## Stop/Start Event ID
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						Stop 0x6001 / Start 0x6002

The upper nibble of byte 6 is 6, which can be used to distinguish this format.
## Undefined/Reserved Event ID’s
Byte 0	Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7
Specific Upper Part						All byte 6 and byte 7 values not defined above

All undefined byte 6 and byte 7 values are reserved for future use. They shall not be sent. If received, they shall be ignored.
# States (Normative)
Each clock has an independent current time, independent running/stopped state and an independent rate.
When the clock is in stopped state, its time is not changing.
When the clock is in running state, its internal time is advancing (rate X) as fast as normal time.
# Interactions (Normative)
In order to ensure that time is only ever represented as an atomic operation, changes in Rate, Year, and/or Date may optionally become valid upon reception of the next Report Time Event or Report Intermediate Time Event.
## Startup
When a clock generator starts to operate, it shall send a Producer Range Identified message covering the whole 16-bit range of the clock’s 6-byte “Specific Upper Part”. Additionally, the clock generator shall send a Producer Identified as Currently Valid message for exactly one the Stop Event ID or the Start Event ID corresponding with its current start/stop state. Clock consumers shall send either a Consumer Range Identified message covering the whole 16-bit range of the clock’s 6-byte “Specific Upper Part” or individual Consumer Identified messages for each individual time event consumed.
### Clock Generator
When a clock on a clock generator is started (from a previously stopped or power up state), upon reception of a Latch Settings Event, or upon reception of a Identify producer message for the Event ID XX.XX.XX.XX.XX.XX.00.00, it shall produce the following events in the following specific order representing a single atomic time:
1. Report Rate
2. Report Year
3. Report Date
4. One of the following events
  1. Report Intermediate Time, if the seconds count is not equal to zero
  2. Report Time, if the seconds count is equal to zero
5. Report Time (continuously as described in section 6.2 below, only if clock is running)
### Clock Consumer
A clock consumer can request the current running state of a clock by sending an Identify Producer message for either of the Start or Stop Clock Events. If a clock generator for the given clock exists, it shall respond with the corresponding Producer Identified as currently Valid or Invalid as appropriate.
## Clock Report
If no consumer of a given clock event has been identified, the clock generator is not required to produce it.
While running, a clock generator shall send a Report Time Event no more frequently than once per real world minute with the following exceptions:
1. When the time rolls over to hour 0 and minute 0, the entire in order sequence described in section 6.1.1 above. This ensures that the year and date are correctly reflected as a result of the rollover.
2. The clock generator has previously received a Consumer Identified message for a specific Report Year, Date, or Time Event, in which case it will always generate this event when appropriate.
It is the responsibility of clock consumers to keep track of intermediate time between Report Time Events. The standard purposely does not define how a clock consumer internally implements time. If a clock consumer wants to get the current time in minute resolution, it shall do so by sending an Identify Producer message using the Event ID XX.XX.XX.XX.XX.XX.50.00.
## Clock Set
Any node may configure a clock generator. It is not a requirement that a clock generator support the capability to change its configuration using events. If Set Rate, Set Year, Set Date, and/or Set Time Event(s) are received, the clock generator does not make the change effective until a Latch Settings Event is received. Upon receiving a Latch Settings Event, the entire in order sequence described in section 6.1.1 above shall be sent by the clock generator.
If a Set Rate Event is received by the clock generator, the clock generator's rate may be, but is not required to be, set to the rate embedded in the event. If the clock producer does not support the requested rate, it shall move to the closest non-zero supported rate. The clock-generator shall subsequently, send the entire in order sequence described in section 6.1.1 above. The rate may be set while the clock is running or stopped.