# Introduction
This explanatory note contains informative discussion and background for the corresponding “OpenLCB CAN Event Transport Specification”. This explanation is not normative in any way.
# Annotations to the Specification
This section provides background information on corresponding sections of the Specification document. It's expected that two documents will be read together.
## Introduction
## Intended Use
## References and Context
 For more information on format and presentation, see:
OpenLCB Common Information Technical Note
## Message Formats
### Producer/Consumer Event Report (PCER)
### Identify Consumer
### Consumer Identified
### Consumer Range Identified
[[[To TN: For example, the event-mask 0xABCD0000 would form the range 0xABCD0000-ABCDFFFF, since the first significant '1' bit is the first low bit of the 'D' hexdigit. Similarly, the event-mask 0xFEDCBFFF would form the range 0xFEDC8000-FEDCBFFF, since 0xB = 0b1011, and the lowest significant '0' bit is in the 3rd digit. The smallest ranges are specified by 0xyyyyyyyE, which specifies a range of 0xyyyyyyyE-0xyyyyyyyF, and 0xyyyyyyyD which specifies 0xyyyyyyyC-0xyyyyyyyF. 0X00000001 gives 0x00000000-0x00000001, and 0x00000002 gives 0x00000000-0x00000002, 0x00000003 gives 0x00000000-0x00000003
Event-Mask	Effective Mask	Bits	#	Resulting Range
0x00000001	0xFFFFFFFE	1	2	0x00000000-0x00000001
0x00000002	0xFFFFFFFE	1	2	0x00000002-0x00000003
0x00000003	0xFFFFFFFC	2	4	0x00000000-0x00000003
0x00000004	0xFFFFFFFC	2	4	0x00000004-0x00000007
0x00000005	0xFFFFFFFE	2	4	0x00000004-0x00000005
0x00ABCDEF	0xFFFFFFF0	4	16	0x00ABCDE0-0x00ABCDEF
0x00ABCDF0	0xFFFFFFF0	4	16	0x00ABCDF0-0x00ABCDFF
0x00ABCDE0	0xFFFFFFE0	5	32	0x00ABCDE0-0x00ABCDFF
0x0000FFFF	0xFFFF0000	16	65k	0x00000000-0x0000FFFF
0xABCD0000	0xFFFF0000	16	65k	0xABCD0000-0xABCDFF / Example of fast clock.FF
0xFFFF0000	0xFFFF0000	16	65k	0xFFFF0000-0xFFFFFFFF

]]]

### Identify Producer
This message is broadcast and requests every node to report whether they produce this event ID.
### Producer Identified
This message is broadcast, in response to a received Identify Producer message, from each node that produces the included event ID. This is one of the messages that allows bridges to do automatic routing of event messages.
### Producer Range Identified
Example of fast clock.
### Identify Events
Coverage of status bits...
Two forms of identify events; recommendation on uses for global form
## States
## Interactions
Nothing prevents extra IdentifyX messages. Nothing prevents combining replies to multiple requests. This allows simplified implementations, for example setting a bit to indicate that a reply can be sent when time/priority is available.
You can query a state when you come up with the request-id message. Conflicting states can happen, and have to be addressed.
Note that the state machine resets with the Initialiation Complete message, not the lower level link (CAN or other) state machine.
Delay in sending the PI/PRI or CI/CRI messages after IC is OK, but there's no delivery guarantee for this nodes events until those have been sent.
When a node changes the events it manages, it still needs to emit the PI/PRI and/or CI/CRI messages. For example, reconfiguration could cause this. It can be handled by sending individual messages, or by resetting and sending them all as part of that.
There is no way to indicate that a node is no longer interested in a particular Event ID. (Sending IC again says that all are not interesting though). This could be added, but it's much harder for gateways to decide an Event ID is not interesting than that it is, because they have to keep a list of all the node IDs that are interested and back that off. Better to just let that the set of interesting event IDs grow until the layout or gateway is reset.
# Background information

Gateways can route this to segments with nodes expressing interest by processing the other event messages. (Gateways section)

Well known events as a mechanism.
Buffering

Ordering & processing
Performance at node startup; layout startup particularly on CAN. Numbers and simulations.
History section:
For monitoring purposes, it was proposed that a PCER message carry a sequence number which increments each time the associated P/C Event ID is sent. It is not at all clear how to do this across nodes, or even across Producers within a single node, as there may be more than one thing that can cause the same P/C Event ID to be sent by a single board;. We decided this would cause more problems than it solved, and omitted it.
There's not room in a CAN frame for both a destination NID and a EID. The protocol has therefore been constructed so that any message carrying an EID (and that isn't a datagram) is globally addressed.