# Introduction
This is about long term operation of really cool trains, not just “better control over DCC”. Still, DCC is an important test case, both with new control hardware (OpenLCB native throttles connected to an OpenLCB-native command station that's generating the DCC signal) and when connected to legacy throttles and/or command stations.
# Annotations to the Standard
## Introduction
Note that this section of the Standard is informative, not normative.
## Intended Use
Note that this section of the Standard is informative, not normative.
## Reference and Context
For more information on format and presentation, see:
OpenLCB Common Information Technical Note
## Speed Control
Rationale: The use of a 16-bit floating point permits relatively precise speed commands, especially at lower speeds; such fine granulatity ensures not just fine-grained control over the locomotive, but helps avoid aliasing issue that arise during the conversion to lower resolution system-specific speed commands (i.e. DCC's 14 or 28-step commands).
The use of meters per second is somewhat arbitrary, and reflects standard velocity units used throughout the metric-speaking world. By standardizing on m/s, we avoid any future unit conversion issues.
The use of scale meters per second has two distinct advantages. First, it permits us to transmit speed commands in a scale-independent way. Second, and because of this, it reduces the number of parameters that must be estimated when controlling a locomotive that has not yet been speed-calibrated (which, for new users using existing digital control systems, will be all of their models). For example, on a DCC system, if I issue a command to proceed at 30mph, the command station must convert the value in the speed command from 30mph to an interger in the range [0-26] (for 28-speed-step control). The command station need only estimate what a reasonable top speed for a locomotive might be: Let us say, 100mph. Thus, the command station could reasonably estimate that 30mph translates to speed step 8.
The alternative possibilities considered to date are absolute speed using real units (as opposed to scale units), and relative speed units. The difficulty with relative speed units (i.e., percentage of full throttle), is that they are ambiguous, and preclude the possibility of performing physical simulations in the cab controller, at least without completely abandoning the particular interpretations assigned to sped values. The difficulty with using real (as opposed to scale) units is that it requires the estimation of an additional parameter for uncalibrated locomotives, specifically the train's scale. If I issue a command to a DCC locomotive to proceed at 0.1 (real)m/s, the command station must not only understand what a reasonable top speed for a train is, but how to scale the speed appropriately, as 0.1 m/s might be quite fast for Z scale, but quite slow for G. As there is really no reasonable scale to use as a default, users must configure their digital command station to set the scale for either the entire layout, or on a per-model basis—an additional configuration step that is easily avoided by the mechanism for scale units described above.
## Function Control
"Functions" like "horn", "headlight", etc are key user features when operating modern decoders. But they're also configuration-like, in that they effect the operation of the device.
How to handle them for a native OpenLCB piece of rolling stock, and for legacy ones via e.g. DCC?
We could take the purist approach and say "configuration is configuration, it's all the same". But that ignores that many people are going to want "Bell" to appear (automatically) on their throttle, but not so many are going to want "Kp back-emf correction factor" to appear there.
People just think about operating and configuring their locomotives as separate things. (Though e.g. "Master Volume" can cross the line)
This doesn't mean that we can't use the same protocol for all other of them. A mixture of memory configuration and CDI should do just fine. It just means that we need to find a way to include clueing information for the throttles on e.g. what to present.
Outputs vs Functions
Tools like DecoderPro and its decoder-definition files make a distinction between "functions", which are the control commands sent via e.g. DCC, and "outputs", which are the things that a decoder can do: Control an electrical output, make a sound, etc. This distinction is useful because one of the configuration options in (some) DCC decoders is a mapping between the functions and the outputs, useful in a world where throttles generally have only about a dozen buttons, but decoders have many output options.
OpenLCB makes a clean separation between functions, which are the control operations, and all configuration & physical information, which lives in the memory configuration and CDI. If there's to be a mapping, it's defined through the CDI.
## Train Configuration
## Train Identification
## Legacy Train Operations
### Node Assignment
### Speed and Function Control
### Configuration
For DCC trains, there are two parts:
- CV access (with the added complexity of indexed and double-indexed Cvs)
- Programmer (main, programming track) control.
# General Information