# Introduction (Informative)
This standard defines a method for Throttle Nodes to find Train Nodes on the network, and for legacy use-cases, instruct an OpenLCB Command Station to create a virtual Train Node given a legacy address and track protocol. This standard is not specific to any wire protocol.
# Intended Use (Informative)
The OpenLCB Traction Protocol describes how a Node acting as throttle can and should control a Node acting as a train. An important component of an ecosystem is how the throttle can find the remote train node that corresponds to the user’s desired locomotive to control. This standard defines one possible method on how to find train nodes from a throttle. As a basic transport this method uses the Event Transport protocol.
In addition to finding already existing Train Nodes, this standard describes an interaction that can be followed by a Command Station to instantiate virtual Nodes in order to act as a gateway between the OpenLCB traction protocol and a legacy track protocol such as DCC.
Note that this standard does not exclude other methods and standards, including some not yet developed, for the same or similar purposes. See the Train Search Protocol Technical Note for some alternatives that were considered or can be employed based on more general enumeration protocols.
TODO: move this discussion to the TN as “Alternatives Considered”:
- A more generic protocol could be developed for searching for Nodes on the network; this may be peer-to-peer or based on a centralized database built and maintained by a single Node that stores details about all Nodes available on the network (including all Train Nodes).
- All Nodes can be enumerated by the unaddressed Verify Node ID Global message. There is no throttling mechanism provisioned to maintain the list of replies with a limited amount of memory. The Node list can then be further processed using Protocol Support Inquiry (PIP) messages to restrict to Train Nodes and Simple Node Information Request (SNIP) messages for querying identifying properties such as train name.
- All Train Nodes can be identified using the Well-Known Event ID IsTrain. There is no throttling mechanism provisioned to maintain the list of replies with a limited amount of memory.
- A legacy track protocol Command Station could expose a command interface either via dedicated OpenLCB messages or via a Datagram-based protocol to maintain it’s list of virtual Train Nodes. This protocol could also be out-of-band, for example through a user interface (physical or HTTP-based), or could be coupled to a persistent database using the Memory Configuration Protocol and the Configuration Descriptor (CDI) XML to expose the user interface via a Configuration Tool.
# References and Context (Normative)
This specification is in the context of the following OpenLCB Standards:
- The Event Transport Standard, which defines the protocol for transporting events, including the messages and interactions for inquiry and discovery of event Producers.
- The Event Identifiers Standard which describes the allocation scheme of Event Identifiers.
For more information on format and presentation, see:
OpenLCB Common Information Technical Note
# Message Formats (Normative)
This standard does not define any OpenLCB messages.
# Allocation (Normative)
## Identifier Range allocation and License terms
For the purpose of the Train Search Protocol the following block of consecutive Event Identifiers is allocated:
09.00.99.FF.00.00.00.00 – 09.00.99.FF.FF.FF.FF.FF
All Event Identifiers in this range are reserved for exclusive use according to the interactions defined by this standard and shall not be used for any other purpose.
The legal entity to whom this Event Identifier range is allocated by the Event Identifiers Standard, Train Control Systems, Inc, hereby grants an irrevocable, non-transferable license to anyone for using the quoted Event Identifiers on the condition, and only so long as, that their use is compliant to this Standard or any later version of it, published by Train Control Systems, Inc.
## Identifier Format
The Event Identifiers in the given range are defined as follows:
Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6	Byte 7	Byte 8
09	00	99	FF	qq	qq	qq	ss
Fixed prefix				Search query / (6 nibbles)			Flags

The search query ‘qq qq qq’ shall be a sequence of 6 nibbles in MSB-first order stored in Bytes 5, 6 and 7 of the Event Identifier. Each individual nibble is one position of the search string:
Search Query Nibble value	Description
0 - 9	The given position of the search term is the given number
0xA - 0xE	Reserved. Do not send, check upon receipt.
0xF	Empty / unused character position. Short queries shall be padded with this nibble value to 6 characters long. Multiple search terms may be concatenated to a search query with this nibble as a separator between them which means the individual terms shall be evaluated with AND relation between them.

The flag byte ‘ss’ is defined as follows:
Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2-0	Description
Allo-cate						0x80: Force allocate legacy node 0: Search only existing nodes
	Exact					0x40: Exact match only / 0: All matches (including partial match)
		Address only				0x20: Match only in address / 0: Match everywhere (address and name)
			Force long address			0x10: Force long address if DCC mode / 0: Use default address type based on the numeric value of the address.
				Reser-ved		Reserved, send as 0, check on receipt.
					Track protocol	0: Any / default track protocol / 1: Märklin-Motorola protocol / 2: Märklin-Motorola 2 protocol / 3: MFX/M4 protocol / 4: DCC 14-speed-step / 5: DCC 28-speed-step / 6: DCC 128-speed-step / 7: Native OpenLCB protocol

# Interactions (Normative)
The following hardware and software nodes are taking part in the interactions presented here:
- The Train Node is an OpenLCB Node that implements the Traction Protocol, controlling a single (physical) train with one or more coupled engines. The hardware implementing the Train Node may be physically built into a model, or it may be built into a centralized gateway hardware that converts to a non-OpenLCB protocol in order to remotely control an engine, for example via Bluetooth or a legacy track protocol such as DCC or Märklin-Motorola. In this case a single piece of hardware may be responsible for representing multiple OpenLCB Nodes on the network.
- The Throttle Node is an OpenLCB Node that intends to send Traction Protocol commands to a desired Train Node. The Throttle Node may be a physical hardware device with a user interface to be used by an operator, a computer software with a user interface for operators to control trains, or a fully automated software.
- The Command Station is a gateway for proxying to some non-OpenLCB protocol, implementing Train Node(s), and having an OpenLCB network connection. There may or may not be a separate OpenLCB Node that represents the Command Station itself on the OpenLCB network.
## Search for existing train nodes
The goal of this use-case is for a Throttle Node to enumerate Train Nodes that exist on the network and match certain criteria. The Throttle Node shall represent the given criteria as an Event Identifier E according to Section 5.2, and set the flag byte Bit 7 (Allocate) to zero (0).
- The Throttle Node shall send an “Identify Producer” message with setting the Event Identifier to E to the network.
- A Train Node upon receipt of an Identify Producer message with an Event Identifier E falling into the Event Identifier Range of Section 5.1, it shall
  - compare its identifying properties to the search criteria represented by the Event Identier E according to Section 6.3;
  - in case of a match, the Train Node shall emit a “Producer Identified” message with the Event Identifier E to the network, setting the Producer validity bits according to Section 6.3;
  - in absence of a match, the Train Node shall not emit a “Producer Identified” message with the Event Identifier E.
## Allocating a new train node
The goal of this use-case is for a Throttle Node to instruct a Command Station to create a new Train Node in the case that no existing Train Node(s) match the search criteria requested by the Throttle Node.
The Throttle Node shall represent the requested address, as an Event Identifier E according to Section 5.2, with setting the flag byte Bit 7 (Allocate) to one (0x80). The Throttle Node may, but is not required to, specify the desired track protocol in the flag byte. It is recommended that the Throttle Node also sets the Bit 6 (Exact) to one (0x40) in the flag byte.
- The Throttle Node shall send an “Identify Producer” message with setting the Event Identifier to E to the network.
- A Command Station upon receipt of an Identify Producer message with an Event Identifier E falling into the Event Identifier Range of Section 5.1 with the flag byte Bit 7 (Allocate) set to one, shall
  - validate that it has the ability to create a Train Node matching its identifying properties to the search criteria represented by the Event Identier E according to Section 6.3;
  - wait at least 200 msec for existing Train Nodes to reply with a “Producer Identified” message;
  - in the absence of such reply, the Command Station shall allocate a new Train Node according to the properties defined by the Event Identifier E, and instruct the new Train Node to emit a “Producer Identified Valid” message with the Event Identifier E.
## Event Identifier matching algorithm
This section defines when an Event Identifier E in the range defined by Section 5.1 matches a Train Node with the identifying properties of <Name, Address, Protocol>.
The Train Node matches the Event Identifier E iff the search query represented by the qq qq qq nibbles of E matches and the requirement by the ss flag byte matches the Protocol and the Flag byte or the query nibbles specify no reserved values marked as “check upon receipt”.
The flag byte ss matches Protocol iff the Legacy Track Protocol field of ss is set to “Any” or Protocol matches the value of the Track Protocol field.
The search query represented by the qq qq qq nibbles of E matches iff
- qq qq qq matches the Address of the Train Node, or
- the Address only bit is not set in the Flag byte ss and qq qq qq matches the Name.
The qq qq qq nibbles of E matches the Address iff qq qq qq contains exactly one contiguous sequence of digit nibbles ‘0’-’9’, and
- the Protocol is non-DCC, or
- the Force long address bit is clear in the Flag byte ss, or
- Address is >= 128, or
- Address is a long address
and
- the Exact bit of the Flag byte ss is set and the decimal value represented by these nibbles is the value of the Address, or
- the Exact bit if the Flag byte ss is clear and the decimal nibbles form a prefix of the decimal representation of Address.

# Section Title
## Subsection Title
### Sub-subsection Title
Praesent gravida pulvinar vehicula. Vivamus eu nisl eget sem rutrum suscipit id a magna. Integer id ante odio.
- Lorem ipsum dolor sit amet, consectetur adipiscing elit.
- Sed consectetur, ipsum et egestas accumsan, felis erat ornare mauris, sit amet suscipit ante orci sed massa.
# Section Title
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.
Quisque sollicitudin tempor bibendum. Donec consectetur condimentum sollicitudin. Sed dignissim velit id felis lacinia at eleifend nisi laoreet. Vivamus tristique porta ornare. Vivamus feugiat dolor id lectus aliquet luctus.