## Slide 1: OpenLCB Traction Protocol
What is it?
Standard set of protocols that allow control of trains on the layout
Not tied to a underlying technology such as NMRA DCC, Märkin Digital, Lionel TMCC, etc.
A Throttle is a node on the OpenLCB network as is the Train
Trains produce a well known Event that identifies them as “I am a Train Node”
Throttles use other protocols to extract information about these trains to:
  Present information to the user for selection
  Run automated scripts for automatic operation
  Anything else that can be imagined

## Slide 2: Elements of the Traction Protocol
Defines generic “actions” a train can do
  Speed
  Direction
  Functions (beyond the common on/off in most DCC decoders such as animations, controlling a trackside crane, etc.)
  Linking Trains together (Consisting)
  Assigning Throttles to Trains
Bi-Directional (Command new state, Query current state)
Defines Function Definition Information (FDI) to create a method of re-definable human readable names and ordering of functions
Defines Train Definition Information (TDI) to create a method of human readable information to help configure the train
  Think of it as JMRI packaged within your locomotive that any OpenLCB throttle can access and use

## Slide 3: Basic Traction Train Assignment
Throttle A
Train
Identify Producers of “IsTrain”
Producer Identified “I’m a Train”
“Reserve”
“Assign Throttle”
“You have me”
Throttle B
“Notify Throttle Changing”
“Allow” (or deny)
“Throttle Assigned”
“Release”
Commands Ignored
Operate and Query the Train

## Slide 4: Enhanced OpenLCB Throttle
Train
“Support FDI?”
“Yes”
“Read FDI via ConfigMem Protocol”
“Set Speed”
“Set Functions”
F0
F1
F2
F3
F4
F5
Sound
Horn
Bell
Whistle
Coupler
Lights
Headlight
Ditch Lights
“Send FDI”
“Query Speed”
Speed
Set= 30km/hr
Commanded = 25.7km/hr
Actual = 22.6km/hr
“Set, Commanded, Actual Speed”
“Query Function”
“Function State/Value”
FDI make sense of Functions
Train state keeps user informed

## Slide 5: Under the Hood
Speed
  16 bit value
  Half float encoding (±65,504)
  Direction encoded in sign bit (-0.0 is valid)
  $FFFF = Not A Number (NaN) used for speed queries that are not supported
    DCC decoders don’t measure actual (ground) or commanded speed (during a momentum ramp up for instance)
    DCC decoders only know the Set Speed
Functions
  24 bit address (16,777,215)
  16 bit value (65,536)

## Slide 6: Protocol at a Glance
Command Group | Command Subgroup | Current State
Set Speed/Direction |  | Implemented and Proven
Set Function |  | Implemented and Proven
Emergency Stop |  | Implemented and Proven
Query Speed |  | Implemented and Proven
Query Function |  | Implemented and Proven
Controller Configuration | Assign | Implemented and Proven
 | Release | Implemented and Proven
 | Query | Implemented and Proven
 | Notify | Implemented and Proven
Consist Configuration | Attach | Next on the Roadmap
 | Detach | Next on the Roadmap
 | Query | Next on the Roadmap
Management | Reserve | Implemented and Proven
 | Release | Implemented and Proven

## Slide 7: Legacy DCC Systems
The Traction Protocol is the future
We have to live in the present
Need to create a way to bridge today into tomorrow
  A Throttle or accessory designed today will work on an OpenLCB Train Node in the future
  A Throttle created today for NMRA DCC bridged to OpenLCB will work on a Märkin Digital system bridge to OpenLCB
Solution was the create a Traction Proxy Protocol
Implements two different functions
  Acts as a “Train Node Server” to create train nodes based on information such as train address, speed steps, etc.
  Acts as a conduit to the backend technology (NMRA DCC, etc.) for Train Nodes that are elsewhere on the OpenLCB network.

## Slide 8: Proxy – Train Node Server
These nodes are unique in they can directly access the legacy link
Throttle A
Legacy Protocol Adapter
Identify Producers of “IsProxy”
Producer Identified “I’m a Proxy”
“Allocate me a Train Node with
Address 3 and 28 Speed Steps”
“Here is a train node ”
Legacy Protocol (DCC)
Train
“Proxy Server”
Use the Traction Protocol
Uses “backdoor” to legacy protocol

## Slide 9: Proxy – Train Proxy
Train Node can live anywhere on the network and can access the legacy protocol through the Train Proxy
Throttle A
Legacy Protocol Adapter
Legacy Protocol (DCC)
Producer Identified “I’m a Train”
Train Node
Identify Producers of “IsTrain”
Use the Traction Protocol
Proxy
Train
“Node”
Direct
Link
Temporarily selects the proxy to the same parameters as the Train
Node to relay the traction protocol command to it

## Slide 10: Protocol at a Glance
Command Group | Command Subgroup | Current State
Allocate Proxy(1) |  | Implemented and Proven
Attach Train ID(2) |  | Implemented and Proven
Detach Train ID(2) |  | Implemented and Proven
Manage Proxy | Reserve | Implemented and Proven
 | Release | Implemented and Proven
(1) Node Server commands
(2) Node Proxy commands
Very simple protocol to bridge today to tomorrow
Ensures that a throttle designed for DCC will work on other systems
  There is a “Suggested Technology” field in the Allocate Proxy command
  There is a “Actual Technology” field in the reply
  This only defines what the passed parameter set is, if the proxy can create a Lionel TMCC using the DCC parameter set it can do so and the throttle does not care!
Ensure throttles designed today will work with Train Nodes of tomorrow

## Slide 11: Conclusion
The Traction Protocols have been in development for almost two years
Numerous inputs and suggestions were discussed and prototyped
It is harder than it looks to meet all the criteria we forced on ourselves
This proposal has not had any roadblocks or dead ends
All goals were met and the statemachines are very simple
What’s next -
  Consisting
  Mapping CVs to Configuration Memory (has been proven out but a complete implementation has not been finished)

## Slide 12: Acknowledgements
The following were instrumental in bringing the Traction Protocol from concept to hardware
  Bob Jacobson
  David Harris
  Don Goodman-Wilson
  Stuart Baker
  Balazs …
  Jim Kueneman
  John Plocher
  Numerous others….

## Slide 13: Links
Overviews
  http://nmranet.org/
  http://openlcb.org/
Traction Protocol Group
  https://groups.yahoo.com/neo/groups/OpenLCBTraction/Info
Traction Protocol Working Notes
  http://sourceforge.net/p/openlcb/svn/HEAD/tree/trunk/specs/drafts/GenTractionWN.pdf
Traction Proxy Protocol Working Notes
  http://sourceforge.net/p/openlcb/svn/HEAD/tree/trunk/specs/drafts/GenTractionProxyWN.pdf