# Introduction (Informative)
This specification describes the format and allocation of OpenLCB node identifiers (node IDs). It is not specific to any wire protocol.
# Intended Use (Informative)
Many OpenLCB protocols rely on each node having a node ID, and those node IDs being absolutely unique between nodes. This Standard is intended to ensure these node IDs are available, and hence applies to all OpenLCB nodes.
# References and Context (Normative)
This specification is in the context of the OpenLCB-CAN … Specification, which specifies …
For more information on format and presentation, see:
OpenLCB Common Information Technical Note
# Format
An OpenLCB node identifier (node ID) shall be six bytes of eight bits each.
The order of bytes in an OpenLCB node ID shall be considered significant. The most-significant byte shall be transmitted first during communication operations. The most-significant byte shall be written first (left-most in Western format) in any human-readable representation.
OpenLCB node IDs shall include one or more 1 bits.
# Allocation
Every OpenLCB node shall have a unique node identifier.
Node identifiers shall be allocated using one of the mechanisms in this section.

## Numbers assigned by manufacturers
## Numbers assigned by members of organized groups
## Numbers assigned by software at run-time
## Numbers assigned using other's methods for assuring uniqueness
## Reserved numbers
Node IDs in the following range shall not be used.

Byte 1	Byte 2	Byte 3	Byte 4	Byte 5	Byte 6
0x00	Any	Any	Any	Any	Any
0xFF	Any	Any	Any	Any	Any

## Number ranges assigned by request