1. NMRAnet TM Introduction
This document describes NMRAnet, a local control bus developed as a parallel to locomotive control, such as DC and DCC.
# 2. Transports
Although NMRAnet is designed to operate on multiple transports, this document will be limited to descriptions of the protocol adapted to CAN and Ethernet.
CAN Standard Version 2.0 A&B shall be adhered to for all signals on the CAN bus. The CAN Extended frame shall be used by NMRAnet to transfer data.
Ethernet standards are adhered to in the adaptation of NMRAnet to it.
# 3. Common Protocol Frame Definition
The Common protocol describes the generalized protocol that is not directed at a specific transport. The following is the Common Protocol Frame Definition:
<MTI:16><sNID:48>{<dNID:48>}{<Flags:8}<Length:16><Data:0-2k>
Where:
MTI – message type indicator
sNID = source node-ID
dNID = destination node-ID
Length – length of data bytes
Data – data associated with the message
## MTI – Message Type Identifier:
<00110><pri:2><0><type:4><0><DID:1><EV:1><Flags:1>
Where:
<00110> - reserved field, must be checked
<pri:2> - priority, 00 is high, 11 is low
<0> - reserved
<type:4> - type of message
<0> - reserved
<DID:1> - Destination node ID indicator, 0=not present, 1=present
<EID:1> - Event ID indicator, 0=not present, 1=present
<FLAGS:1> - flags-byte indicator, 0=not present, 1=present
Notes:
1. If the DID is present, it must be mappable to the full NID., and is located at the start of the data-part;
2. If the EID is present, it follows the EID, if present, else is located at the start of the data-part;
3. If the flag-byte is present, the low bits of it may be relocated in CAN messages.
## sNID – Source Node ID:
The can be the full node ID (48-bits) or an alias on some transports, such as CAN. It must be translatable between the two forms.
## dNID – Destination Node ID:
This is an optional field, and its presence is indicated by the DID-bit in the MTI.
## Event ID:
This is an optional field, and its presence is indicated by the EID-bit in the MTI.
## Flags-byte:
This is an optional field, and its presence is indicated by the Flags-bit in the MTI.
## Data:
This is an optional field, and can be up to 2k in length.
# 4. Common Protocol
The common Protocol has three basic message types:
- Events: <00110><pri:2><0><xxxx><0010><sNID><event#>
- Datagrams: <00110><pri:2><0><yyyy><0z00><sNID>{<dNID>}<data:0-2k>
- Streams: <00110><pri:2><0><zzzz><0100><sNID><dNID><data:0-2k>
# 5. CAN Protocol
The CAN-specific adaptation of the Common Protocol is described in this section.
The general CAN format used is the 29-bit variant:
[<header:29>](<length:4>) <datapart:0-64>
Where:
<header:29> - 29-bit header, enclosed in []
<lenght:4> - number of data bytes, enclosed in ()
<datapart:0-64> - data-bytes, 0-8
The description of the OpenLCB CAN packets uses the following abbreviations:
- NIDa – a 12-bit alias for the full NID (node ID)
- sNIDa – the soure-node-ID's alias
- dNIDa – the destination-node-ID's alias
- format – 3-bit field that determines the packet format
- type– 8-bit message type indicator
- flags – 4-bit field that carries specific message flag bits
## Forms:
Adaptation of the OpenLCB Common Protocol messages uses a general form:	[<format:3><variableField:12><sNIDa>](len:4>)<data:0-64>
 This is divided into two main sub-forms, with different uses for the variableField:
- Those messages without a source-node ID:	[<format:3><type:8><flags:4><sNIDa>](len:4>)<data:0-64>
- And those with a source-node ID:
  [<format:3><dNIDa:12><sNIDa>](len:4>)<mti:8><data:0-56>
## Formats:
The 3-bit format field determines how the rest of the packet is interpreted:
- 0 0b000 Simple MTI
- 1 0b001 Complex MTI, includes full source node ID
- 2 0b010 reserved
- 3 0b011 reserved
- 4 0b100 Datagram frame fragment, continuing
- 5 0b101 Datagram frame, last fragment
- 6 0b110 Destination, non-stream
- 7 0b111 Destination, stream
## Basic Messages:
This section describes the three basic types of messages that as a basis for operation and layered protocols.
Events
Event-messages implement Producer-Consumer Events. They are the work-horse of operations and implement m:n relationships. They are also used for embedded information, such as fast-clock-time, and to port other foreign event protocols to OpenLCB by embedding.
[<pri><0><0x02D><sNIDa:12>]<8><event:64>
Datagrams
Datagrams are used to sent small amounts of data, between 1 and 72 bytes, between nodes. Since CAN packets are limited to a 8-byte datapart, the Common Message Datagram is implemented as a set of 'middle'-packets, and ending with an 'end'-packet.
   Middle packets:
[<pri><4><sNIDa:12><dNIDa:12>](<len:4>)<data:0-64>
    End packet:
[<pri><5><sNIDa><dNIDa>](<len:4>)<data:8-64>
Streams
Streams are designed for sending large amounts of data between two nodes as a continuous stream of messages. CAN packets are limited to 8-bytes in the datapart. Because of buffering concerns, strams involve a significant set-up overhead in order to negotiate buffer-sizes across multiple segments. These stream-management packets are described later.
[<pri><7><dNIDa:12><sNIDa:12>](<len:4>)<data:0-64>

## Management Messages:
Initialization complete
This packet indicates that a node has completed its initialization.
[<pri><1><0x008><sNIDa>](6) NID
Verify Node ID Number
Request verification responses from a specific or all nodes.
[<pri><6><dNIDa><sNIDa>](1) 0x0A – specific node
[<pri><0><0x0AF><sNIDa>](0)	- all nodes
Verified Node ID Number
Requset a response wrt its node ID from a specific node.
[<pri><1><0x0BF><sNIDa>](6) NID
Optional Interaction Rejected
This packet indicates that a node can not participate in a protocol.
[<pri><6><dNIDa><sNIDa>](2) 0x0C MTI
Terminate Due to Error
This indicates that a node cannot proceed with a protocol.
[<pri><6><dNIDa><sNIDa>](2) 0x0D MTI
Event Exchange Messages
Identify Consumers
Request nodes report interest in an event, as a consumer.
[<pri><0><0x24F><sNIDa>](8) EID
Consumer Identify Range
A node reporting interest in a range of events, as a consumer, as indicated by a mask.
[<pri><1><0x25F><sNIDa>](8) Event-mask
Consumer Identified
A node is reporting interest in an event, as a consumer.
[<pri><1><0x26><11vu><sNIDa>](8) EID
Identify Producer
Request nodes report interest in an event, as a producer.
[<pri><0><0x28F><sNIDa>](8) EID
Producer Identify Range
A node is reporting interest in a range of events, as a producer, as indicated by a mask.
[<pri><1><0x29F><sNIDa>](8) Event-mask
Producer Identified
A node is reporting interest in an event, as a consumer.
[<pri><1><0x2A><11vu><sNIDa>](8) EID
Identify Events
Request to report all events, to a specific or all nodes.
[<pri><6><dNIDa><sNIDa>](1) 0x2B – specific node
[<pri><0><0x02B><sNIDa>](0) - all nodes
Learn Event
Teach a specific event to all nominated event slots.
[<pri><0><0x2CF><sNIDa>](8) EID
P/C Event Report (event message)
Basic event packet.
[<pri><0><0x2DF><sNIDa>](8) EID