# Introduction (Informative)
This specification describes the format and allocation of OpenLCB node identifiers (node IDs). It is not specific to any wire protocol.
# References and Context (Informative)
This specification is in the context of the OpenLCB-CAN … Specification, which specifies …
For more information on format and presentation, see:
OpenLCB Common Information Technical Note
# Format
An OpenLCB node identifier (node ID) shall be six bytes of eight bits each.
The order of bytes in an OpenLCB node ID shall be considered significant. The most-significant byte shall be transmitted first during communication operations. The most-significant byte shall be written first (left-most in Western format) in any human-readable representation.
OpenLCB node IDs shall include one or more 1 bits.
# Allocation

Below this is just a collection of pieces from other docs right now.