Summary of Changes to LCC Documents 2024-07-22
### New Documents for Public Comment
S-9.7.4.6-TrainControl-2024-07-22.pdf
TN-9.7.4.6-TrainControl-2024-07-22.pdf

S-9.7.4.7-TrainSearch-2024-07-22.pdf
TN-9.7.4.7-TrainSearch-2024-07-22.pdf

S-9.7.4.8-FunctionDefinitionInformation-2024-07-22.pdf
TN-9.7.4.8-FunctionDefinitionInformation-2024-07-22.pdf
### Documents with Changes for Public Comment
S-9.7.0.3-UniqueIdentifiers-2024-07-22.pdf
TN-9.7.0.3-UniqueIdentifiers-2024-07-22.pdf
  - Updates ranges for various train control systems: DC, DCC, TMCC, etc

S-9.7.0.4-EventIdentifiers-2024-07-22.pdf
TN-9.7.0.4-EventIdentifiers-2024-07-22.pdf
  - Adds Train Search protocol event range
  - Adds 11-bit extended DCC accessory address range
  - Reformat some tables

S-9.7.1.1-CanPhysical-2024-07-22.pdf
TN-9.7.1.1-CanPhysical-2024-07-22.pdf
  - Add a section on Electronic Labeling
  - Add a section on Injection Current
  - Added discussion of CAN bit timing
  - Standardize the use of ALT_L/ALT_H for the NMRA S-9.1.2 DCC signal
  - Clarify discussion of gateways and repeaters

S-9.7.2.1-CanFrameTransfer-2024-07-22.pdf
TN-9.7.2.1-CanFrameTransfer-2024-07-22.pdf
  - Add to the behavior of the AME Message
  - Fix calculation error in the example provided in the TN.

S-9.7.3-MessageNetwork-2024-07-22.pdf
TN-9.7.3-MessageNetwork-2024-07-22.pdf
  - Update the table of PIP bits
  - Clarifies the content of the OIR message
  - Clarified the discussion of priorities

S-9.7.3.1-EventTransport-2024-07-22.pdf
TN-9.7.3.1-EventTransport-2024-07-22.pdf
  - Add Events with Payload

S-9.7.4.1-ConfigurationDescriptionInformation-2024-07-22.pdf
TN-9.7.4.1-ConfigurationDescriptionInformation-2024-07-22.pdf
  - The size of integer variables is restricted to 1, 2 or 4 bytes
  - Define signed vs unsigned behavior of integer variables
  - The requirement that unused bytes in a String variable be set to null has been removed
  - Addition of float variables
  - Discussion of possible ways of representing group names

S-9.7.4.2-MemoryConfiguration-2024-07-22.pdf
TN-9.7.4.2-MemoryConfiguration-2024-07-22.pdf
  - Remove the write-size bits in the Configuration Options Reply
  - Add stream reads to a Configuration Options Reply bit

S-9.7.4.3-SimpleNodeInformation-2024-07-22.pdf
TN-9.7.4.3-SimpleNodeInformation-2024-07-22.pdf
  - Update how the two data blocks are versioned

### Documents that have not changed since 2021-04-25 (for completeness)
There were no changes to these documents since 2021-04-25 but they are included here for completeness
TN-9.7.0.1-Glossary-2021-04-25.pdf

TN-9.7.0.2-CommonInformation-2021-04-25.pdf

S-9.7.3.2-DatagramTransport-2021-04-25.pdf
TN-9.7.3.2-DatagramTransport-2021-04-25.pdf

S-9.7.4.4-FirmwareUpgrade-2021-04-25.pdf
TN-9.7.4.4-FirmwareUpgrade-2021-04-25.pdf

S-9.7.4.5-BroadcastTime-2021-04-25.pdf
TN-9.7.4.5-BroadcastTime-2021-04-25.pdf